## Slide 1: About the Presentations
The presentations cover the objectives found in the opening of each chapter.
All chapter objectives are listed in the beginning of each presentation.
You may customize the presentations to fit your class needs.
Some figures from the chapters are included. A complete set of images from the book can be found on the Instructor Resources disc.

## Slide 2: Network+ Guide to Networks 6th Edition
Chapter 1
An Introduction to Networking

## Slide 3: Objectives
List the advantages of networked computing relative to stand-alone computing
Distinguish between client/server and peer-to-peer networks
List elements common to all client/server networks

## Slide 4: Objectives (cont’d.)
Describe several specific uses for a network
Identify some of the certifications available to networking professionals
Identify the kinds of skills and specializations that will help you excel as a networking professional

## Slide 5: Why Use Networks?
Network
  Group of computers and devices
    Connected by transmission media
Stand-alone computer
  Not connected to other computers
  Uses local software and data
Advantages of networks
  Device sharing by multiple users
    Saves money and time
  Central network management

## Slide 6: Types of Networks
Models vary according to:
  Computer positioning
  Control levels over shared resources
  Communication and resource sharing schemes
Network models
  Peer-to-peer
  Client/server

## Slide 7: Peer-to-Peer Networks
Direct computer communication
  Equal authority
Individual resource sharing
  May share resources
  May prevent access to resources
Traditional model
  Two or more general purpose computers:
    Capable of sending and receiving information to and from every other computer

## Slide 8: Peer-to-Peer Networks (cont’d.)
Figure 1-1 Resource sharing on a simple peer-to-peer network
Courtesy Course Technology/Cengage Learning

## Slide 9: Peer-to-Peer Networks (cont’d.)
Advantages
  Simple configuration
  Less expensive
    Compared to other network models
Disadvantages
  Not flexible
  Not necessarily secure
  Not practical for large installations

## Slide 10: Peer-to-Peer Networks (cont’d.)
Resource sharing method
  Modify file sharing controls
    User responsibility
  Not centrally controlled
    Access may not be uniform or secure
Environments
  Small home or office
  Large networks using the Internet
    Gnutella, Bitcoin, original Napster
    BitTorrent software

## Slide 11: Client/Server Networks
Server
  Central computer
  Facilitates communication and resource sharing
Clients
  Personal computers
  Also known as workstations
Central resource sharing controlled by server
  Sharing data, storage space, devices
  No direct sharing of client resources

## Slide 12: Client/Server Networks (cont’d.)
Computer roles
  Server
  Clients
    Run local applications
    Store data locally
    Use server shared applications, data, devices
    Use server as intermediary
Communication
  Switches or routers

## Slide 13: Client/Server Networks (cont’d.)
Figure 1-2 Resource sharing on a client/server network
Courtesy Course Technology/Cengage Learning

## Slide 14: Client/Server Networks (cont’d.)
Server requirement
  Network operating system
    Manages client data, resources
    Ensures authorized user access
    Controls user file access
    Restricts user network access
    Dictates computer communication rules
    Supplies application to clients
Server examples
  UNIX, Linux, Microsoft Server 2008 R2, MAC OS X Server

## Slide 15: Client/Server Networks (cont’d.)
Server features relative to clients
  More memory, processing, storage capacity
  Equipped with special hardware
    Provides network management functions
Disadvantages relative to peer-to-peer networks
  Complex design and maintenance

## Slide 16: Client/Server Networks (cont’d.)
Advantages relative to peer-to-peer networks
  User credential assigned from one place
  Multiple shared resource access centrally controlled
  Central problem monitoring, diagnostics, correction capabilities
  Optimized to handle heavy processing loads
  Can connect many computers on a network
  More scalable

## Slide 17: LANs, MANs, and WANs
LAN (local area network)
  Network confined to a relatively small space
  1980s
    LANs became popular as peer-to-peer based
  Today
    Larger and more complex client/server network
MAN (metropolitan area network)
  Connects clients and servers from multiple buildings
  Uses different transmission media and technology than LAN

## Slide 18: LANs, MANs, and WANs (cont’d.)
Figure 1-3 Interconnected LANs
Courtesy Course Technology/Cengage Learning

## Slide 19: LANs, MANs, and WANs (cont’d.)
WAN (wide area network)
  Connects two or more geographically distinct LANs or MANs
  Uses different transmission methods and media than LAN
  Network connection
    Separate offices in same organization
    Separate offices in different organizations

## Slide 20: LANs, MANs, and WANs (cont’d.)
Figure 1-4 A simple WAN
Courtesy Course Technology/Cengage Learning

## Slide 21: Elements Common to Client/Server Networks
Client
  Network computer requesting resources or services from another network computer
  Client workstation human user
  Client software installed on workstation
Server
  Network computer managing shared resources
  Runs network operating software
Workstation
  Personal computer
    May or may not be connected to network

## Slide 22: Elements Common to Client/Server Networks (cont’d.)
NIC (network interface card)
  Device inside computer
  Connects computer to network media
  Allows communication with other computers
NOS (network operating system)
  Server software
  Enables server to manage data, users, groups, security, applications, and other networking functions

## Slide 23: Elements Common to Client/Server Networks (cont’d.)
Figure 1-5 A NIC (network interface card)
Courtesy Course Technology/Cengage Learning

## Slide 24: Elements Common to Client/Server Networks (cont’d.)
Host
  Computer
  Enables network resource sharing by other computers
Node
  Client, server, or other device
  Communicates over a network
  Identified by unique network address
Connectivity device
  Allows multiple networks or multiple parts of one network to connect and exchange data

## Slide 25: Elements Common to Client/Server Networks (cont’d.)
Segment
  Group of nodes
  Uses same communications channel for traffic
Backbone
  Connects segments and significant shared devices
  “A network of networks”
Topology
  Computer network physical layout
  Ring, bus, star or hybrid formation

## Slide 26: Elements Common to Client/Server Networks (cont’d.)
Courtesy Course Technology/Cengage Learning
Figure 1-6 A LAN backbone

## Slide 27
Courtesy Course Technology/Cengage Learning
Figure 1-7 Common network topologies

## Slide 28: Elements Common to Client/Server Networks (cont’d.)
Protocol
  Standard method or format for communication between networked devices
Packet
  Distinct data units exchanged between nodes
Addressing
  Scheme for assigning unique identifying number to every node
Transmission media
  Means through which data is transmitted and received

## Slide 29
Courtesy Course Technology/Cengage Learning
Figure 1-8 Examples of network transmission media

## Slide 30: How Networks Are Used
Network services
  Functions provided by a network
  E-mail
  Printer sharing
  File sharing
  Internet access and Web site delivery
  Remote access capabilities
  Voice (telephone) and video services
  Network management

## Slide 31: File and Print Services
File services
  Capability of server to share data files, applications and disk storage space
File server
  Provides file services
File services provide foundation of networking
Print services
  Share printers across network
  Saves time and money

## Slide 32: Access Services
Allow remote user network connection
Allow network users to connect to machines outside the network
Remote user
  Computer user on different network or in different geographical location from LAN’s server
Network operating systems include built-in access services

## Slide 33: Access Services (cont’d.)
Provide LAN connectivity when WAN connection is not cost-effective
External staff can diagnose problems
Allow external users to use network resources and devices
  Same as if logged on to office workstation

## Slide 34: Communications Services
Convergence
  Offering multiple types of communications services on the same network
Unified communications
  Centralized management of multiple network-based communications
Mail server
  Computer responsible for e-mail storage and transfer

## Slide 35: Communications Services (cont’d.)
Additional tasks of mail servers
  Intercept spam
  Handle objectionable content
  Route messages according to rules
  Provide Web-based client for checking e-mail
  Notify administrators or users if certain events occur
  Schedule e-mail transmission, retrieval, storage, maintenance
  Communicate with mail servers on other networks
Mail server runs specialized mail server software

## Slide 36: Internet Services
Web server
  Computer installed with appropriate software to supply Web pages to many different clients upon demand
Other Internet services
  File transfer capabilities
  Internet addressing schemes
  Security filters
  Means for directly logging on to other Internet computers

## Slide 37: Management Services
Small network management
  Single network administrator
Today’s larger network management
  Centrally administered network management tasks

## Slide 38: Management Services (cont’d.)
Important network management services
  Traffic monitoring and control
  Load balancing
  Hardware diagnosis and failure alert
  Asset management
  License tracking
  Security auditing
  Address management
  Backup and restoration of data

## Slide 39: Becoming a Networking Professional
Job market
  Many job postings for computer professionals
  Expertise levels required vary
To prepare for entering job market:
  Master general networking technologies
  Select and study areas of interest
  Hone communication and teamwork skills
  Stay abreast of emerging technologies
  Consider professional certification
  Get to know others in your field

## Slide 40: Mastering the Technical Challenges
Skills to acquire
  Installing, configuring, troubleshooting network server and client hardware and software
  Understanding characteristics of transmission media
  Understanding network design
  Understanding network protocols
  Understanding how users interact with network
  Constructing a network with clients, servers, media, and connectivity devices

## Slide 41: Mastering the Technical Challenges (cont’d.)
Pick one or two areas of concentration
Specialties currently in high demand
  Network security
  Convergence
  In-depth knowledge about one or more NOSs
    UNIX, Linux, MAC OS X Server, Microsoft Windows Server 2008 R2
  Network management
  Wireless network design
  Configuration of routers and switches
  Centralized data storage and management

## Slide 42: Developing Your “Soft Skills”
Soft skills
  Not easily measurable
  Important to networking projects
Examples of soft skills
  Customer relations
  Oral and written communications
  Dependability
  Teamwork
  Leadership abilities

## Slide 43: Pursuing Certification
Certification process
  Mastering specific material
    Hardware system, operating system, programming language, software application
  Proving mastery
    Pass exams
Professional organizations
  CompTIA
    Network+
Vendors
  Microsoft , Cisco

## Slide 44: Pursuing Certification (cont’d.)
Benefits
  Better salary
  Greater opportunities
  Professional respect
  Access to better support

## Slide 45: Finding a Job in Networking
Job research methods
  Search the Web
  Check local newspaper’s Web site
  Visit a career center
  Network with like-minded professionals
  Attend career fairs
  Enlist a recruiter

## Slide 46: Joining Professional Associations
Benefits of professional associations
  Connect with people having similar interests
  New learning opportunities
  Specialized information access
  Tangible assets (free goods)
  Access to publications
  Technical workshops and conferences
  Free software, pre-release software
  Hardware lab access

## Slide 47: Joining Professional Associations (cont’d.)
Table 1-1 Some networking organizations
Courtesy Course Technology/Cengage Learning

## Slide 48: Summary
Network
  Group of connected computers and other devices
Types of networks include peer-to-peer and client/server networks
LANs, MANs, and WANs describe different sizes of networks
  May use different transmission media and technology
Networks provide a wide range of services
  Examples: file and print sharing

## Slide 49: Summary (cont’d.)
Network management services centrally administer management tasks on a network
  Examples: hardware problem diagnosis, license tracking
Job preparation
  Master broad networking skills
  Choose one or two specialty areas
  Consider benefits of certification