## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 4
Introduction to TCP/IP Protocols

## Slide 2: Objectives
Identify and explain the functions of the core TCP/IP protocols
Explain the TCP/IP model and how it corresponds to the OSI model
Discuss addressing schemes for TCP/IP in IPv4 and IPv6 and explain how addresses are assigned automatically using DHCP (Dynamic Host Configuration Protocol)

## Slide 3: Objectives (cont’d.)
Describe the purpose and implementation of DNS (Domain Name System)
Identify the well-known ports for key TCP/IP services
Describe how common Application layer TCP/IP protocols are used

## Slide 4: Characteristics of TCP/IP (Transmission Control Protocol/Internet Protocol)
Protocol Suite
  Referred to as “IP” or “TCP/IP”
  Subprotocols include TCP, IP, UDP, ARP
Developed by US Department of Defense
  ARPANET (1960s)
    Internet precursor

## Slide 5: Characteristics of TCP/IP (cont’d.)
Advantages of TCP/IP
  Open nature
    Costs nothing to use
  Flexible
    Runs on virtually any platform
    Connects dissimilar operating systems and devices
  Routable
    Transmissions carry Network layer addressing information
    Suitable for large networks

## Slide 6: The TCP/IP Model
Four layers
  Application layer
  Transport layer
  Internet layer
  Network access layer (or Link layer)

## Slide 7
Figure 4-1 The TCP/IP model compared with the OSI model
Courtesy Course Technology/Cengage Learning

## Slide 8: The TCP/IP Core Protocols
TCP/IP suite subprotocols
Operate in Transport or Network layers of OSI model
Provide basic services to protocols in other layers
Most significant protocols in TCP/IP suite
  TCP
  IP

## Slide 9: TCP (Transmission Control Protocol)
Transport layer protocol
Provides reliable data delivery services
  Connection-oriented subprotocol
    Establish connection before transmitting
Uses sequencing and checksums
Provides flow control
TCP segment format
  Encapsulated by IP packet in Network layer
    Becomes IP packet’s “data”

## Slide 10
Figure 4-2 A TCP segment
Courtesy Course Technology/Cengage Learning

## Slide 11
Table 4-1 Fields in a TCP segment
Courtesy Course Technology/Cengage Learning

## Slide 12
Figure 4-3 TCP segment data
Courtesy Course Technology/Cengage Learning

## Slide 13: TCP (cont’d.)
Three segments establish connection
Computer A issues message to Computer B
  Sends segment with SYN bit set
    SYN field: Random synchronize sequence number
Computer B receives message
  Sends segment
    ACK field: sequence number Computer A sent plus 1
    SYN field: Computer B random number

## Slide 14: TCP (cont’d.)
Computer A responds
  Sends segment
    ACK field: sequence number Computer B sent plus 1
    SYN field: Computer B random number
FIN flag indicates transmission end

## Slide 15
Figure 4-4 Establishing a TCP connection
Courtesy Course Technology/Cengage Learning

## Slide 16: UDP (User Datagram Protocol)
Transport layer protocol
Provides unreliable data delivery services
  Connectionless transport service
  No assurance packets received in correct sequence
  No guarantee packets received at all
  No error checking, sequencing
  Lacks sophistication
    More efficient than TCP
Useful situations
  Great volume of data transferred quickly

## Slide 17
Figure 4-5 A UDP segment
Courtesy Course Technology/Cengage Learning

## Slide 18: IP (Internet Protocol)
Network layer protocol
  How and where data delivered, including:
    Data’s source and destination addresses
Enables TCP/IP to internetwork
  Traverse more than one LAN segment
    More than one network type through router
Network layer data formed into packets
  IP packet
    Data envelope
    Contains information for routers to transfer data between different LAN segments

## Slide 19: IP (cont’d.)
Two versions
  IPv4: unreliable, connectionless protocol
  IPv6
Newer version of IPv6
  IP next generation
  Released in 1998
Advantages of IPv6
  Provides billions of additional IP addresses
  Better security and prioritization provisions

## Slide 20
Figure 4-6 An IPv4 packet
Courtesy Course Technology/Cengage Learning

## Slide 21
Figure 4-8 An IPv6 packet header
Courtesy Course Technology/Cengage Learning

## Slide 22: IGMP (Internet Group Management Protocol)
Operates at Network layer of OSI model
Manages multicasting on networks running IPv4
Multicasting
  Point-to-multipoint transmission method
  One node sends data to a group of nodes
  Used for Internet teleconferencing or videoconferencing

## Slide 23: ARP (Address Resolution Protocol)
Network layer protocol
Used with IPv4
Obtains MAC (physical) address of host or node
Creates database that maps MAC to host’s IP address
ARP table
  Table of recognized MAC-to-IP address mappings
  Saved on computer’s hard disk
  Increases efficiency
  Contains dynamic and static entries

## Slide 24: ICMP (Internet Control Message Protocol)
Network layer protocol
  Reports on data delivery success/failure
Announces transmission failures to sender
  Network congestion
  Data fails to reach destination
  Data discarded: TTL expired
ICMP cannot correct errors
  Provides critical network problem troubleshooting information
ICMPv6 used with IPv6

## Slide 25: IPv4 Addressing
Networks recognize two addresses
  Logical (Network layer)
  Physical (MAC, hardware) addresses
IP protocol handles logical addressing
Specific parameters
  Unique 32-bit number
    Divided into four octets (sets of eight bits) separated by periods
    Example: 144.92.43.178
  Network class determined from first octet

## Slide 26
Table 4-4 Commonly used TCP/IP classes
Courtesy Course Technology/Cengage Learning

## Slide 27: IPv4 Addressing (cont’d.)
Class D, Class E rarely used (never assign)
  Class D: value between 224 and 239
    Multicasting
  Class E: value between 240 and 254
    Experimental use
Eight bits have 256 combinations
  Networks use 1 through 254
  0: reserved as placeholder
  255: reserved for broadcast transmission

## Slide 28: IPv4 Addressing (cont’d.)
Class A devices
  Share same first octet (bits 0-7)
    Network ID
  Host: second through fourth octets (bits 8-31)
Class B devices
  Share same first two octet (bits 0-15)
  Host: second through fourth octets (bits 16-31)
Class C devices
  Share same first three octet (bits 0-23)
  Host: second through fourth octets (bits 24-31)

## Slide 29
Figure 4-11 IPv4 addresses and their classes
Courtesy Course Technology/Cengage Learning

## Slide 30: IPv4 Addressing (cont’d.)
Loop back address
  First octet equals 127 (127.0.0.1)
Loopback test
  Attempting to connect to own machine
  Powerful troubleshooting tool
Windows XP, Vista
  ipconfig command
Unix, Linux
  ifconfig command

## Slide 31: Binary and Dotted Decimal Notation
Dotted decimal notation
  Common way of expressing IP addresses
  Decimal number between 0 and 255 represents each octet
  Period (dot) separates each decimal
Dotted decimal address has binary equivalent
  Convert each octet
  Remove decimal points

## Slide 32: Subnet Mask
32-bit number identifying a device’s subnet
Combines with device IP address
Informs network about segment, network where device attached
Four octets (32 bits)
  Expressed in binary or dotted decimal notation
Assigned same way as IP addresses
  Manually or automatically (via DHCP)

## Slide 33: Subnet Mask (cont’d.)
Courtesy Course Technology/Cengage Learning
Table 4-5 Default subnet masks

## Slide 34: IPv6 Addressing
Composed of 128 bits
Eight 16-bit fields
Typically represented in hexadecimal numbers
  Separated by a colon
  Example: FE22:00FF:002D:0000:0000:0000:3012:CCE3
Abbreviations for multiple fields with zero values
  00FF can be abbreviated FF
  0000 can be abbreviated 0

## Slide 35: IPv6 Addressing (cont’d.)
Multicast address
  Used for transmitting data to many different devices simultaneously
Anycast address
  Represents any one interface from a group of interfaces
Modern devices and operating systems can use both IPv4 and IPv6

## Slide 36: Assigning IP Addresses
Government-sponsored organizations
  Dole out IP addresses
  IANA, ICANN, RIRs
Companies, individuals
  Obtain IP addresses from ISPs
Every network node must have unique IP address
  Error message otherwise

## Slide 37: Assigning IP Addresses (cont’d.)
Static IP address
  Manually assigned
  To change: modify client workstation TCP/IP properties
  Human error causes duplicates
Dynamic IP address
  Assigned automatically
  Most common method
    Dynamic Host Configuration Protocol (DHCP)

## Slide 38: DHCP (Dynamic Host Configuration Protocol)
  Automatically assigns device a unique IP address
Application layer protocol
Reasons for implementing
  Reduce time and planning for IP address management
  Reduce potential for error in assigning IP addresses
  Enable users to move workstations and printers
  Make IP addressing transparent for mobile users

## Slide 39: DHCP (cont’d.)
DHCP leasing process
  Device borrows (leases) an IP address while attached to network
Lease time
  Determined when client obtains IP address at log on
  User may force lease termination
DHCP service configuration
  Specify leased address range
  Configure lease duration
Several steps to negotiate client’s first lease

## Slide 40
Courtesy Course Technology/Cengage Learning
Figure 4-14 The DHCP leasing process

## Slide 41: DHCP (cont’d.)
Terminating a DHCP Lease
  Expire based on period established in server configuration
  Manually terminated at any time
    Client’s TCP/IP configuration
    Server’s DHCP configuration
Circumstances requiring lease termination
  DHCP server fails and replaced
DHCP services run on several server types
  Installation and configurations vary

## Slide 42: Private and Link-Local Addresses
Private addresses
  Allow hosts in organization to communicate across internal network
  Cannot be routed on public network
Specific IPv4 address ranges reserved for private addresses
Link-local address
  Provisional address
  Capable of data transfer only on local network segment

## Slide 43: Private and Link-Local Addresses (cont’d.)
Zero configuration (Zeroconf)
  Collection of protocols that assign link-local addresses
  Part of computer’s operating software
Automatic private IP addressing (APIPA)
  Service that provides link-local addressing on Windows clients

## Slide 44: Sockets and Ports
Processes assigned unique port numbers
Process’s socket
  Port number plus host machine’s IP address
Port numbers
  Simplify TCP/IP communications
  Ensures data transmitted correctly
Example
  Telnet port number: 23
  IPv4 host address: 10.43.3.87
  Socket address: 10.43.3.87:23

## Slide 45
Courtesy Course Technology/Cengage Learning
Figure 4-15 A virtual connection for the telnet service

## Slide 46: Sockets and Ports (cont’d.)
Port number range: 0 to 65535
Three types
  Well Known Ports
    Range: 0 to 1023
    Operating system or administrator use
  Registered Ports
    Range: 1024 to 49151
    Network users, processes with no special privileges
  Dynamic and/or Private Ports
    Range: 49152 through 65535
    No restrictions

## Slide 47
Courtesy Course Technology/Cengage Learning
Table 4-6 Commonly used TCP/IP port numbers

## Slide 48: Host Names and DNS (Domain Name System)
TCP/IP addressing
  Long, complicated numbers
  Good for computers
People remember words better
  Internet authorities established Internet node naming system
Host
  Internet device
Host name
  Name describing device

## Slide 49: Domain Names
Domain
  Group of computers belonging to same organization
  Share common part of IP address
Domain name
  Identifies domain (loc.gov)
  Associated with company, university, government organization
Fully qualified host name (blogs.loc.gov)
  Local host name plus domain name

## Slide 50: Domain Names (cont’d.)
Label (character string)
  Separated by dots
  Represents level in domain naming hierarchy
Example: www.google.com
  Top-level domain (TLD): com
  Second-level domain: google
  Third-level domain: www
Second-level domain
  May contain multiple third-level domains
ICANN established domain naming conventions

## Slide 51
Courtesy Course Technology/Cengage Learning
Table 4-7 Some well-known top-level domains

## Slide 52: Domain Names (cont’d.)
ICANN approved over 240 country codes
Host and domain names restrictions
  Any alphanumeric combination up to 253 characters
  Include hyphens, underscores, periods in name
  No other special characters

## Slide 53: Host Files
ARPAnet used HOSTS.TXT file
  Associated host names with IP addresses
  Host matched by one line
    Identifies host’s name, IP address
    Alias provides nickname
UNIX-/Linux-based computer
  Host file called hosts, located in the /etc directory
Windows computer
  Host file called hosts
  Located in Windows\system32\drivers\etc folder

## Slide 54
Courtesy Course Technology/Cengage Learning
Figure 4-16 Sample host file

## Slide 55: DNS (Domain Name System)
Hierarchical
  Associate domain names with IP addresses
DNS refers to:
  Application layer service accomplishing association
  Organized system of computers, databases making association possible
DNS redundancy
  Many computers across globe related in hierarchical manner
  Root servers
    13 computers (ultimate authorities)

## Slide 56: DNS (cont’d.)
Three components
  Resolvers
    Any hosts on Internet needing to look up domain name information
  Name servers (DNS servers)
    Databases of associated names, IP addresses
    Provide information to resolvers on request
  Namespace
    Abstract database of Internet IP addresses, associated names
    Describes how name servers of the world share DNS information

## Slide 57
Courtesy Course Technology/Cengage Learning
Figure 4-17 Domain name resolution

## Slide 58: DNS (cont’d.)
Resource record
  Describes one piece of DNS database information
  Many different types
    Dependent on function
Table 4-8 Common DNS record types
Courtesy Course Technology/Cengage Learning

## Slide 59: Configuring DNS
Large organizations
  Often maintain two name servers
    Primary and secondary
  Ensures Internet connectivity
DHCP service assigns clients appropriate addresses
Occasionally may want to manually configure
  Follow steps on Pages 172-173 in the text

## Slide 60: DDNS (Dynamic DNS)
Used in Website hosting
  Manually changing DNS records unmanageable
Process
  Service provider runs program on user’s computer
    Notifies service provider when IP address changes
  Service provider’s server launches routine to automatically update DNS record
    Effective throughout Internet in minutes
Not DNS replacement
Larger organizations buy statically assigned IP address

## Slide 61: Application Layer Protocols
Work over TCP or UDP plus IP
  Translate user requests into format readable by network
HTTP
  Application layer protocol central to using Web
DHCP
  Automatic address assignment
Additional Application layer protocols exist

## Slide 62: Telnet
Terminal emulation protocol
  Log on to remote hosts
    Using TCP/IP protocol suite
  TCP connection established
    Keystrokes on user’s machine act like keystrokes on remotely connected machine
Often connects two dissimilar systems
Can control remote host
Drawback
  Notoriously insecure

## Slide 63: FTP (File Transfer Protocol)
Send and receive files via TCP/IP
Host running FTP server portion
  Accepts commands from host running FTP client
FTP commands
  Operating system’s command prompt
    No special client software required
FTP hosts allow anonymous logons
Secure FTP (SFTP)
  More secure version of FTP
  Will be covered in Chapter 11

## Slide 64: TFTP (Trivial File Transfer Protocol)
Enables file transfers between computers
  Simpler (more trivial) than FTP
TFTP relies on Transport layer UDP
  Connectionless
  Does not guarantee reliable data delivery
No ID or password required
  Security risk
No directory browsing allowed
Useful to load data, programs on diskless workstation

## Slide 65: NTP (Network Time Protocol)
Synchronizes network computer clocks
Depends on UDP Transport layer services
  Benefits from UDP’s quick, connectionless nature
    Time sensitive
    Cannot wait for error checking
Time synchronization importance
  Routing
  Time-stamped security methods
  Maintaining accuracy, consistency between multiple storage systems

## Slide 66: PING (Packet Internet Groper)
Provides verification
  TCP/IP installed, bound to NIC, configured correctly, communicating with network
  Host responding
Uses ICMP services
  Send echo request and echo reply messages
    Determine IP address validity
Ping IP address or host name
Ping loopback address: 127.0.0.1
  Determine if workstation’s TCP/IP services running

## Slide 67: PING (cont’d.)
Operating system determines PING command options, switches, syntax
Courtesy Course Technology/Cengage Learning
Figure 4-19 Output from successful and unsuccessful PING

## Slide 68: Summary
Protocols define standards for network communication
  TCP/IP suite most popular
TCP: connection-oriented subprotocol
UDP: efficient, connectionless service
IP provides information about how and where to deliver data
IPv4 addresses: unique 32-bit numbers
IPv6 addresses: composed of eight 16-bit fields
DHCP assigns addresses automatically
DNS tracks domain names and their addresses