## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 7
Wide Area Networks

## Slide 2: Objectives
Identify a variety of uses for WANs
Explain different WAN topologies, including their advantages and disadvantages
Compare the characteristics of WAN technologies, including their switching type, throughput, media, security, and reliability
Describe several WAN transmission and connection methods, including PSTN, ISDN, T-carriers, DSL, broadband cable, broadband over powerline, ATM, and SONET

## Slide 3: WAN Essentials
WAN
  Network traversing some distance, connecting LANs
  Transmission methods depend on business needs
WAN and LAN common properties
  Client-host resource sharing
  Layer 3 and higher protocols
  Packet-switched digitized data

## Slide 4: WAN Essentials (cont’d.)
WAN and LAN differences
  Layers 1 and 2 access methods, topologies, media
  LAN wiring: privately owned
  WAN wiring: public through NSPs (network service providers)
    Examples: AT&T, Verizon, Sprint
WAN site
  Individual geographic locations connected by WAN
WAN link
  WAN site to WAN site connection

## Slide 5: WAN Topologies
Differences from LAN topologies
  Distance covered, number of users, traffic
  Connect sites via dedicated, high-speed links
    Use different connectivity devices
WAN connections
  Require Layer 3 devices
    Routers
  Cannot carry nonroutable protocols

## Slide 6
Figure 7-1 Differences in LAN and WAN connectivity
Courtesy Course Technology/Cengage Learning

## Slide 7: Bus
Bus topology WAN
  Each site connects serially to two sites maximum
  Network site dependent on every other site to transmit and receive traffic
  Different locations connected to another through point-to-point links
Best use
  Organizations requiring small WAN, dedicated circuits
Drawback
  Not scalable

## Slide 8
Figure 7-2 A bus topology WAN
Courtesy Course Technology/Cengage Learning

## Slide 9: Ring
Ring topology WAN
  Each site connected to two other sites
  Forms ring pattern
  Connects locations
  Relies on redundant rings
    Data rerouted upon site failure
  Expansion
    Difficult, expensive
Best use
  Connecting maximum five locations

## Slide 10
Figure 7-3 A ring topology WAN
Courtesy Course Technology/Cengage Learning

## Slide 11: Star
Star topology WAN
  Single site central connection point
  Separate data routes between any two sites
Advantages
  Single connection failure affects one location
  Shorter data paths between any two sites
  Expansion: simple, less costly
Drawback
  Central site failure can bring down entire WAN

## Slide 12
Figure 7-4 A star topology WAN
Courtesy Course Technology/Cengage Learning

## Slide 13: Mesh
Mesh topology WAN
  Incorporates many directly interconnected sites
  Data travels directly from origin to destination
  Routers can redirect data easily, quickly
Most fault-tolerant WAN type
Full-mesh WAN
  Every WAN site directly connected to every other site
  Drawback: cost
Partial-mesh WAN
  Less costly

## Slide 14
Figure 7-5 Full-mesh and partial-mesh WANs
Courtesy Course Technology/Cengage Learning

## Slide 15: Tiered
Tiered topology WAN
  Sites connected in star or ring formations
    Interconnected at different levels
  Interconnection points organized into layers
    Form hierarchical groupings
Flexibility
  Allows many variations, practicality
  Requires careful considerations
    Geography, usage patterns, growth potential

## Slide 16
Figure 7-6 A tiered topology WAN
Courtesy Course Technology/Cengage Learning

## Slide 17: PSTN
PSTN (Public Switched Telephone Network)
  Network of lines, carrier equipment providing telephone service
  POTS (plain old telephone service)
  Encompasses entire telephone system
  Originally: analog traffic
  Today: digital data, computer controlled switching
Dial-up connection
  Modem connects computer to distant network
    Uses PSTN line

## Slide 18: PSTN (cont’d.)
PSTN elements
  Cannot handle digital transmission
    Requires modem
Signal travels path between modems
  Over carrier’s network
    Includes CO (central office), remote switching facility
    Signal converts back to digital pulses
CO (central office)
  Where telephone company terminates lines
  Switches calls between different locations

## Slide 19: PSTN (cont’d.)
Local loop (last mile)
  Portion connecting residence, business to nearest CO
  May be digital or analog
Digital local loop
  Fiber to the home (fiber to the premises)
Passive optical network (PON)
  Carrier uses fiber-optic cabling to connect with multiple endpoints

## Slide 20
Figure 7-7 A long-distance dial-up connection
Courtesy Course Technology/Cengage Learning

## Slide 21
Figure 7-8 Local loop portion of the PSTN
Courtesy Course Technology/Cengage Learning

## Slide 22: PSTN (cont’d.)
Optical line terminal
  Single endpoint at carrier’s central office in a PON
  Device with multiple optical ports
Optical network unit
  Distributes signals to multiple endpoints using fiber-optic cable
    Or copper or coax cable

## Slide 23
Figure 7-9 Passive optical network (PON)
Courtesy Course Technology/Cengage Learning

## Slide 24: X.25 and Frame Relay
X.25 ITU standard
  Analog, packet-switching technology
    Designed for long distance
  Original standard: mid 1970s
    Mainframe to remote computers: 64 Kbps throughput
  Update: 1992
    2.048 Mbps throughput
    Client, servers over WANs
  Verifies transmission at every node
    Excellent flow control, ensures data reliability
    Slow, unreliable for time-sensitive applications

## Slide 25: X.25 and Frame Relay (cont’d.)
Frame relay
  Updated X.25: digital, packet-switching
  Protocols operate at Data Link layer
    Supports multiple Network, Transport layer protocols
Both perform error checking
  Frame relay: no reliable data delivery guarantee
  X.25: errors fixed or retransmitted
Throughput
  X.25: 64 Kbps to 45 Mbps
  Frame relay: customer chooses

## Slide 26: X.25 and Frame Relay (cont’d.)
Both use virtual circuits
  Node connections with disparate physical links
    Logically appear direct
  Advantage: efficient bandwidth use
Both configurable as SVCs (switched virtual circuits)
  Connection established for transmission, terminated when complete
Both configurable as PVCs (permanent virtual circuits)
  Connection established before transmission, remains after transmission

## Slide 27: X.25 and Frame Relay (cont’d.)
PVCs
  Not dedicated, individual links
X.25 or frame relay lease contract
  Specify endpoints, bandwidth
  CIR (committed information rate)
    Minimum bandwidth guaranteed by carrier
PVC lease
  Share bandwidth with other X.25, frame relay users

## Slide 28
Figure 7-10 A WAN using frame relay
Courtesy Course Technology/Cengage Learning

## Slide 29: X.25 and Frame Relay (cont’d.)
Frame relay lease advantage
  Pay for bandwidth required
  Less expensive technology
  Long-established worldwide standard
Frame relay and X.25 disadvantage
  Throughput variability on shared lines
Frame relay and X.25 easily upgrade to T-carrier dedicated lines
  Same connectivity equipment

## Slide 30: ISDN
Standard for transmitting digital data over PSTN
Gained popularity: 1990s
  Connecting WAN locations
    Exchanges data, voice signals
Protocols at Physical, Data Link, Transport layers
  Signaling, framing, connection setup and termination, routing, flow control, error detection and correction
Relies on PSTN for transmission medium
Dial-up or dedicated connections
  Dial-up relies exclusively on digital transmission

## Slide 31: ISDN (cont’d.)
Capability: two voice calls, one data connection on a single line
Two channel types
  B channel: “bearer”
    Circuit switching for voice, video, audio: 64 Kbps
  D channel: “data”
    Packet-switching for call information: 16 or 64 Kbps
BRI (Basic Rate Interface) connection
PRI (Primary Rate Interface) connection

## Slide 32: ISDN (cont’d.)
BRI: two B channels, one D channel (2B+D)
  B channels treated as separate connections
    Carry voice and data
Bonding
  Two 64-Kbps B channels combined
    Achieve 128 Kbps
PRI: 23 B channels, one 64-Kbps D channel (23B+D)
  Separate B channels independently carry voice, data
  Maximum throughput: 1.544 Mbps
PRI and BRI may interconnect

## Slide 33
Figure 7-11 A BRI link
Courtesy Course Technology/Cengage Learning

## Slide 34
Figure 7-12 A PRI link
Courtesy Course Technology/Cengage Learning

## Slide 35: T-Carriers
T1s, fractional T1s, T3s
Physical layer operation
Single channel divided into multiple channels
  Uses TDM (time division multiplexing) over two wire pairs
Medium
  Telephone wire, fiber-optic cable, wireless links

## Slide 36: Types of T-Carriers
Many available
  Most common: T1 and T3
Table 7-1 Carrier specifications
Courtesy Course Technology/Cengage Learning

## Slide 37: Types of T-Carriers (cont’d.)
T1: 24 voice or data channels
  Maximum data throughput: 1.544 Mbps
T3: 672 voice or data channels
  Maximum data throughput: 44.736 Mbps (45 Mbps)
T-carrier speed dependent on signal level
  Physical layer electrical signaling characteristics
  DS0 (digital signal, level 0)
    One data, voice channel

## Slide 38: Types of T-Carriers (cont’d.)
T1 use
  Connects branch offices, connects to carrier
  Connects telephone company COs, ISPs
T3 use
  Data-intensive businesses
T3 provides 28 times more throughput (expensive)
  Multiple T1’s may accommodate needs
TI costs vary by region
Fractional T1 lease
  Use some T1 channels, charged accordingly

## Slide 39: T-Carrier Connectivity
T-carrier line requires connectivity hardware
  Customer site, switching facility
  Purchased or leased
  Cannot be used with other WAN transmission methods
T-carrier line requires different media
  Throughput dependent

## Slide 40: T-Carrier Connectivity (cont’d.)
Wiring
  Plain telephone wire
    UTP or STP copper wiring
    STP preferred for clean connection
  Coaxial cable, microwave, fiber-optic cable
  T1s using STP require repeater every 6000 feet
  Multiple T1s or T3
    Fiber-optic cabling

## Slide 41
Figure 7-13 T1 wire terminations in an RJ-48 connector
Courtesy Course Technology/Cengage Learning

## Slide 42
Figure 7-14 T1 crossover cable terminations
Courtesy Course Technology/Cengage Learning

## Slide 43: T-Carrier Connectivity (cont’d.)
CSU/DSU (Channel Service Unit/Data Service Unit)
  Two separate devices
  Combined into single stand-alone device
    Interface card
  T1 line connection point
CSU
  Provides digital signal termination
  Ensures connection integrity

## Slide 44: T-Carrier Connectivity (cont’d.)
DSU
  Converts T-carrier frames into frames LAN can interpret (and vice versa)
  Connects T-carrier lines with terminating equipment
  Incorporates multiplexer
Smart jack
  Terminate T-carrier wire pairs
    Customer’s demarc (demarcation point)
    Inside or outside building
  Connection monitoring point

## Slide 45
Figure 7-17 A point-to-point T-carrier connection
Courtesy Course Technology/Cengage Learning

## Slide 46: T-Carrier Connectivity (cont’d.)
Incoming T-carrier line
  Multiplexer separates combined channels
Outgoing T-carrier line
  Multiplexer combines multiple LAN signals
Terminal equipment
  Switches, routers
  Best option: router, Layer 3 or higher switch
    Accepts incoming CSU/DSU signals
    Translates Network layer protocols
    Directs data to destination

## Slide 47: T-Carrier Connectivity (cont’d.)
CSU/DSU may be integrated with router, switch
  Expansion card
  Faster signal processing, better performance
  Less expensive, lower maintenance solution

## Slide 48
Figure 7-18 A T-carrier connecting to a LAN through a router
Courtesy Course Technology/Cengage Learning

## Slide 49: DSL (Digital Subscriber Line)
Operates over PSTN
Directly competes with ISDN, T1 services
Requires repeaters for longer distances
Best suited for WAN local loop
Supports multiple data, voice channels
  Over single line
  Higher, inaudible telephone line frequencies
Uses advanced data modulation techniques
  Data signal alters carrier signal properties
  Amplitude or phase modulation

## Slide 50: Types of DSL
xDSL refers to all DSL varieties
  ADSL, G.Lite, HDSL, SDSL, VDSL, SHDSL
Two DSL categories
  Asymmetrical and symmetrical
Downstream
  Data travels from carrier’s switching facility to customer
Upstream
  Data travels from customer to carrier’s switching facility

## Slide 51: Types of DSL (cont’d.)
Downstream, upstream throughput rates may differ
  Asymmetrical
    More throughput in one direction
    Downstream throughput higher than upstream throughput
    Best use: video conferencing, web surfing
  Symmetrical
    Equal capacity for upstream, downstream data
    Examples: HDSL, SDSL, SHDSL
    Best use: uploading, downloading significant data amounts

## Slide 52: Types of DSL (cont’d.)
DSL types vary
  Data modulation techniques
  Capacity
  Distance limitations
  PSTN use
Table 7-2 Comparison of DSL types
Courtesy Course Technology/Cengage Learning

## Slide 53: DSL Connectivity
ADSL: common example on home computer
  Establish TCP connection
  Transmit through DSL modem
    Internal or external
    Splitter separates incoming voice, data signals
    May connect to switch or router

## Slide 54: DSL Connectivity (cont’d.)
ADSL (cont’d.)
  DSL modem forwards modulated signal to local loop
    Signal continues over four-pair UTP wire
    Distance less than 18,000 feet: signal combined with other modulated signals in telephone switch
  Carrier’s remote switching facility
    Splitter separates data signal from voice signals
    Request sent to DSLAM (DSL access multiplexer)
    Request issued from carrier’s network to Internet backbone

## Slide 55
Figure 7-20 A DSL connection
Courtesy Course Technology/Cengage Learning

## Slide 56: DSL Connectivity (cont’d.)
DSL competition
  T1, ISDN, broadband cable
DSL installation
  Hardware, monthly access costs
    Slightly less than ISDN; significantly less than T1s
DSL drawbacks
  Throughput lower than broadband cable

## Slide 57: Broadband Cable
Cable companies connectivity option
Based on TV signals coaxial cable wiring
  Theoretical transmission speeds
    150 Mbps downstream; 10 Mbps upstream
  Real transmission
    10 Mbps downstream; 2 Mbps upstream
    Transmission limited ( throttled)
    Shared physical connections
Best uses
  Web surfing
  Network data download

## Slide 58: Broadband Cable (cont’d.)
Cable modem
  Modulates, demodulates transmission, reception signals via cable wiring
  Operates at Physical and Data Link layer
  May connect to connectivity device
Figure 7-21 A cable modem
Courtesy Zoom Telephonics, Inc.

## Slide 59: Broadband Cable (cont’d.)
Infrastructure required
  HFC (hybrid fiber-coax)
    Expensive fiber-optic link supporting high frequencies
    Connects cable company’s offices to node
  Cable drop
    Connects node to customer’s business or residence
    Fiber-optic or coaxial cable
    Connects to head end
Provides dedicated connection
Many subscribers share same local line, throughput

## Slide 60
Figure 7-22 Cable infrastructure
Courtesy Course Technology/Cengage Learning

## Slide 61: BPL (Broadband Over Powerline)
High-speed Internet access over the electrical grid
  Began around 2000
Advantages
  Potential for reaching remote users
Roadblocks to development
  Opposition from telecommunications groups
  Costly infrastructure upgrades
  Signals subject to more noise than DSL, cable
  Signals interfere with amateur radio

## Slide 62: ATM (Asynchronous Transfer Mode)
Functions in Data Link layer
Asynchronous communications method
  Nodes do not conform to predetermined schemes
    Specifying data transmissions timing
  Each character transmitted
    Start and stop bits
Specifies Data Link layer framing techniques
Fixed packet size
  Packet (cell)
    48 data bytes plus 5-byte header

## Slide 63: ATM (cont’d.)
Smaller packet size requires more overhead
  Decrease potential throughput
  Cell efficiency compensates for loss
ATM relies on virtual circuits
  ATM considered packet-switching technology
  Virtual circuits provide circuit switching advantage
  Reliable connection
Allows specific QoS (quality of service) guarantee
  Important for time-sensitive applications

## Slide 64: ATM (cont’d.)
Compatibility
  Other leading network technologies
  Cells support multiple higher-layer protocol
  LANE (LAN Emulation)
    Allows integration with Ethernet, token ring network
    Encapsulates incoming Ethernet or token ring frames
    Converts to ATM cells for transmission
Throughput: 25 Mbps to 622 Mbps
Cost: relatively expensive

## Slide 65: SONET (Synchronous Optical Network)
Key strengths
  WAN technology integration
  Fast data transfer rates
  Simple link additions, removals
  High degree of fault tolerance
Synchronous
  Data transmitted and received by nodes must conform to timing scheme
Advantage
  Interoperability

## Slide 66
Figure 7-23 A SONET ring
Courtesy Course Technology/Cengage Learning

## Slide 67: SONET (cont’d.)
Fault tolerance
  Double-ring topology over fiber-optic cable
SONET ring
  Begins, ends at telecommunications carrier’s facility
  Connects organization’s multiple WAN sites in ring fashion
  Connect with multiple carrier facilities
    Additional fault tolerance
  Terminates at multiplexer
    Easy SONET ring connection additions, removals

## Slide 68
Figure 7-24 SONET connectivity
Courtesy Course Technology/Cengage Learning

## Slide 69: SONET (cont’d.)
Data rate indicated by OC (Optical Carrier) level
Table 7-3 SONET OC levels
Courtesy Course Technology/Cengage Learning

## Slide 70: SONET (cont’d.)
Implementation
  Large companies
  Long-distance companies
    Linking metropolitan areas and countries
  ISPs
    Guarantying fast, reliable Internet access
  Telephone companies
    Connecting Cos
Best uses: audio, video, imaging data transmission
Expensive to implement

## Slide 71: WAN Technologies Compared
Table 7-4 A comparison of WAN technology throughputs
Courtesy Course Technology/Cengage Learning

## Slide 72: Summary
WAN topologies: bus, ring, star, mesh, tiered
PSTN network provides telephone service
FTTP uses fiber-optic cable to complete carrier connection to subscriber
High speed digital data transmission
  Physical layer: ISDN, T-carriers, DSL, SONET
  Data Link layer: X.25, frame relay, ATM
  Physical and Data link: broadband