## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 8
Wireless Networking

## Slide 2: Objectives
Explain how nodes exchange wireless signals
Identify potential obstacles to successful wireless transmission and their repercussions, such as interference and reflection
Understand WLAN (wireless LAN) architecture

## Slide 3: Objectives (cont’d.)
Specify the characteristics of popular WLAN transmission methods, including 802.11 a/b/g/n
Install and configure wireless access points and their clients
Describe wireless WAN technologies, including 802.16 (WiMAX), HSPA+, LTE, and satellite communications

## Slide 4: The Wireless Spectrum
Continuum of electromagnetic waves
  Data, voice communication
  Arranged by frequencies
    Lowest to highest
  Spans 9 KHz and 300 GHz
Wireless services associated with one area
FCC oversees United States frequencies
ITU oversees international frequencies
  Air signals propagate across borders

## Slide 5
Figure 8-1 The wireless spectrum
Courtesy Course Technology/Cengage Learning

## Slide 6: Characteristics of Wireless Transmission
Similarities with wired
  Layer 3 and higher protocols
  Signal origination
    From electrical current, travel along conductor
Differences from wired
  Signal transmission
    No fixed path, guidance
Antenna
  Signal transmission and reception
  Same frequency required on each antenna

## Slide 7
Figure 8-2 Wireless transmission and reception
Courtesy Course Technology/Cengage Learning

## Slide 8: Antennas
Radiation pattern
  Relative strength over three-dimensional area
    Of all electromagnetic energy that antenna sends, receives
Directional antenna
  Issues wireless signals along single direction
Omnidirectional antenna
  Issues, receives wireless signals
    Equal strength, clarity in all directions
Range
  Reachable geographical area

## Slide 9: Signal Propagation
LOS (line-of-sight)
  Signal travels in straight line
    Directly from transmitter to receiver
Obstacles affect signal travel; signals may:
  Pass through them
  Be absorbed into them
  Be subject to three phenomena
    Reflection: bounce back to source
    Diffraction: splits into secondary waves
    Scattering: diffusion in multiple different directions

## Slide 10: Signal Propagation (cont’d.)
Multipath signals
  Wireless signals follow different paths to destination
  Caused by reflection, diffraction, scattering
  Advantage
    Better chance of reaching destination
  Disadvantage
    Signal delay

## Slide 11
Figure 8-3 Multipath signal propagation
Courtesy Course Technology/Cengage Learning

## Slide 12: Signal Degradation
Fading
  Variation in signal strength
    Electromagnetic energy scattered, reflected, diffracted
Attenuation
  Signal weakens
    Moving away from transmission antenna
  Correcting signal attenuation
    Amplify (analog), repeat (digital)
Noise
  Significant problem
    No wireless conduit, shielding

## Slide 13: Frequency Ranges
2.4-GHz band (older)
  Frequency range: 2.4–2.4835 GHz
  11 unlicensed communications channels
  Susceptible to interference
Unlicensed: no FCC registration required
5-GHz band (newer)
  Frequency bands
    5.1 GHz, 5.3 GHz, 5.4 GHz, 5.8 GHz
  24 unlicensed bands, each 20 MHz wide
  Used by weather, military radar communications

## Slide 14: Narrowband, Broadband, and Spread-Spectrum Signals
Narrowband
  Transmitter concentrates signal energy at single frequency, very small frequency range
Broadband
  Relatively wide wireless spectrum band
  Higher throughputs than narrowband
Spread-spectrum
  Multiple frequencies used to transmit signal
  Offers security

## Slide 15: Narrowband, Broadband, and Spread-Spectrum Signals (cont’d.)
FHSS (frequency hopping spread spectrum)
  Signal jumps between several different frequencies within band
  Synchronization pattern known only to channel’s receiver, transmitter
DSSS (direct-sequence spread spectrum)
  Signal’s bits distributed over entire frequency band at once
  Each bit coded
    Receiver reassembles original signal upon receiving bits

## Slide 16
Figure 8-4 FHSS (frequency hopping spread spectrum)
Courtesy Course Technology/Cengage Learning

## Slide 17
Figure 8-5 DSSS (direct sequence spread spectrum)
Courtesy Course Technology/Cengage Learning

## Slide 18: Fixed versus Mobile
Fixed communications wireless systems
  Transmitter, receiver locations do not move
  Transmitting antenna focuses energy directly toward receiving antenna
    Point-to-point link results
  Advantage
    No wasted energy issuing signals
    More energy used for signal itself
Mobile communications wireless systems
  Receiver located anywhere within transmitter’s range

## Slide 19: WLAN (Wireless LAN) Architecture
Ad hoc WLAN
  Wireless nodes transmit directly to each other
  Use wireless NICs
    No intervening connectivity device
  Poor performance
    Many spread out users, obstacles block signals
Wireless access point (WAP)
  Accepts wireless signals from multiple nodes
    Retransmits signals to network
  Base stations, wireless routers, wireless gateways

## Slide 20: WLAN Architecture (cont’d.)
Infrastructure WLAN
  Stations communicate with access point
    Not directly with each other
  Access point requires sufficient power, strategic placement
WLAN may include several access points
  Dependent upon number of stations
  Maximum number varies: 10-100

## Slide 21
Figure 8-7 An infrastructure WLAN
Courtesy Course Technology/Cengage Learning

## Slide 22: WLAN Architecture (cont’d.)
Mobile networking allows roaming wireless nodes
  Range dependent upon wireless access method, equipment manufacturer, office environment
    Access point range: 300 feet maximum
Can connect two separate LANs
  Fixed link, directional antennas between two access points
    Allows access points 1000 feet apart
Support for same protocols, operating systems as wired LANs
  Ensures compatibility

## Slide 23
Figure 8-8 Wireless LAN interconnection
Courtesy Course Technology/Cengage Learning

## Slide 24: 802.11 WLANs
Wireless technology standards
  Describe unique functions
    Physical and Data Link layers
  Differences between standards
    Specified signaling methods, geographic ranges, frequency usages
  Most popular: developed by IEEE’s 802.11 committee
Notable Wi-Fi standards
  802.11b, 802.11a, 802.11g, 802.11n
  Share characteristics
    Half-duplexing, access method

## Slide 25: Access Method
802.11 MAC services
  Append 48-bit (6-byte) physical addresses to frame
    Identifies source, destination
Same physical addressing scheme as 802.3
  Allows easy combination
Wireless devices
  Not designed to simultaneously transmit and receive
  Cannot quickly detect collisions
  Use different access method

## Slide 26: Access Method (cont’d.)
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
  Minimizes collision potential
  Uses ACK packets to verify every transmission
    Requires more overhead than 802.3
    Real throughput less than theoretical maximum
RTS/CTS (Request to Send/Clear to Send) protocol
  Optional
  Ensures packets not inhibited by other transmissions
  Efficient for large transmission packets
  Further decreases overall 802.11 efficiency

## Slide 27
Figure 8-9 CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance
Courtesy Course Technology/Cengage Learning

## Slide 28: Association
Packet exchanged between computer and access point
  Gain Internet access
Scanning
  Surveys surroundings for access point
  Active scanning transmits special frame
    Probe
  Passive scanning listens for special signal
    Beacon fame

## Slide 29: Association (cont’d.)
SSID (service set identifier)
  Unique character string identifying access point
    In beacon frame information
  Configured in access point
  Better security, easier network management
BSS (basic service set)
  Station groups sharing access point
  BSSID (basic service set identifier)
    Station group identifier

## Slide 30: Association (cont’d.)
ESS (extended service set)
  Access point group connecting same LAN
    Share ESSID (extended service set identifier)
  Allows roaming
    Station moving from one BSS to another without losing connectivity
Several access points detected
  Select strongest signal, lowest error rate
  Poses security risk
    Powerful, rogue access point

## Slide 31
Figure 8-10 A network with a single BSS
Courtesy Course Technology/Cengage Learning

## Slide 32
Figure 8-11 A network with multiple BSSs forming an ESS
Courtesy Course Technology/Cengage Learning

## Slide 33: Association (cont’d.)
ESS with several authorized access points
  Must allow station association with any access point
    While maintaining network connectivity
Reassociation
  Mobile user moves from one access point’s range into another’s range
  Occurs by simply moving; high error rate
Stations’ scanning feature
  Used to automatically balance transmission loads
    Between access points

## Slide 34: Frames
802.11 networks overhead
  ACKs, probes, and beacons
802.11 specifies MAC sublayer frame type
Multiple frame type groups
  Control: medium access and data delivery
    ACK and RTS/CTS frames
  Management: association and reassociation
  Data: carry data sent between stations

## Slide 35
Figure 8-12 Basic 802.11 data frame compared with an 802.3 (Ethernet) frame
Courtesy Course Technology/Cengage Learning

## Slide 36: Frames (cont’d.)
802.11 data frame overhead
  Four address fields
    Source address, transmitter address, receiver address, and destination address
  Sequence Control field
    How large packet fragmented
  Frame Control field
Wi-Fi share MAC sublayer characteristics
Wi-Fi differ in modulation methods, frequency usage, and range

## Slide 37: 802.11b
2.4-GHz band
  Separated into 22-MHz channels
Throughput
  11-Mbps theoretical
  5-Mbps actual
100 meters node limit
Oldest, least expensive
Being replaced by 802.11g

## Slide 38: 802.11a
Released after 802.11b
5-GHz band
  Not congested like 2.4-GHz band
    Lower interference, requires more transmit power
Throughput
  54 Mbps theoretical
  11 and 18 Mbps effective
20 meter node limit
Requires additional access points
Rarely preferred

## Slide 39: 802.11g
Affordable as 802.11b
Throughput
  54 Mbps theoretical
  20 to 25 Mbps effective
100 meter node range
2.4-GHz frequency band
  Compatible with 802.11b networks

## Slide 40: 802.11n
Standard ratified in 2009
Primary goal
  Wireless standard providing much higher effective throughput
Maximum throughput: 600 Mbps
  Threat to Fast Ethernet
Backward compatible with 802.11a, b, g standards

## Slide 41: 802.11n (cont’d.)
2.4-GHz or 5-GHz frequency range
Compared with 802.11a, 802.11g
  Same data modulation techniques
Compared with three 802.11 standards
  Manages frames, channels, and encoding differently
    Allows high throughput

## Slide 42: 802.11n (cont’d.)
MIMO (multiple input-multiple output)
  Multiple access point antennas may issue signal to one or more receivers
  Increases network’s throughput, access point’s range
Figure 8-13 802.11n access point with three antennas
Courtesy Cisco Systems, Inc.

## Slide 43: 802.11n (cont’d.)
Channel bonding
  Two adjacent 20-MHz channels bonded to make 40-MHz channel
    Doubles the bandwidth available in single 20-MHz channel
    Bandwidth reserved as buffers assigned to carry data
Higher modulation rates
  Single channel subdivided into multiple, smaller channels
    More efficient use of smaller channels
    Different encoding methods

## Slide 44: 802.11n (cont’d.)
Frame aggregation
  Combine multiple frames into one larger frame
  Advantage: reduces overhead
Figure 8-15 Aggregated 802.11n frame
Courtesy Course Technology/Cengage Learning

## Slide 45: 802.11n (cont’d.)
Maximum throughput dependencies
  Number and type of strategies used
  2.4-GHz or 5-GHz band
  Actual throughput: 65 to 600 Mbps
Backward compatible
  Not all 802.11n features work
Recommendation
  Use 802.11n-compatible devices

## Slide 46
Table 8-1 Wireless standards
Courtesy Course Technology/Cengage Learning

## Slide 47: Implementing a WLAN
Designing a small WLAN
  Home, small office
Formation of larger, enterprise-wide WANs
Installing and configuring access points and clients
Implementation pitfalls

## Slide 48: Determining the Design
One access point
  Combine with switching, routing functions
  Connects wireless clients to LAN
  Acts as Internet gateway
Access point WLAN placement considerations
  Typical distances between access point and client
  Obstacles
    Type and number of, between access point and clients

## Slide 49
Figure 8-16 Home or small office WLAN arrangement
Courtesy Course Technology/Cengage Learning

## Slide 50: Determining the Design (cont’d.)
Larger WLANs
  Systematic approach to access point placement
Site survey
  Assesses client requirements, facility characteristics, coverage areas
  Determines access point arrangement ensuring reliable wireless connectivity
    Within given area
  Proposes access point testing
    Test wireless access from farthest corners

## Slide 51: Determining the Design (cont’d.)
Install access points
  Must belong to same ESS, share ESSID
Enterprise-wide WLAN design considerations
  How wireless LAN portions will integrate with wired portions

## Slide 52
Figure 8-17 Enterprise-wide WLAN
Courtesy Course Technology/Cengage Learning

## Slide 53: Configuring Wireless Connectivity Devices
Access point CD-ROM or DVD
  Guides through setup process
Variables set during installation
  Administrator password
  SSID
  Whether or not DHCP is used
  Whether or not the SSID is broadcast
  Security options

## Slide 54: Configuring Wireless Clients
Configuration varies from one client type to another
Linux and UNIX clients wireless interface configuration
  Use graphical interface
  iwconfig command-line function
    View, set wireless interface parameters

## Slide 55
Figure 8-18 Output from iwconfig command
Courtesy Course Technology/Cengage Learning

## Slide 56: Avoiding Pitfalls
Access point versus client configurations
  SSID mismatch
  Incorrect encryption
  Incorrect channel, frequency
  Standard mismatch (802.11 a/b/g/n)
Incorrect antenna placement
  Verify client within 330 feet
Interference
  Check for EMI sources

## Slide 57: Wireless WANs
Wireless broadband
  Latest wireless WAN technologies
  Specifically designed for:
    High-throughput; long-distance digital data exchange

## Slide 58: 802.16 (WiMAX)
WiMAX (Worldwide Interoperability for Microwave Access)
  Most popular version: 802.16e (2005)
  Improved WiMAX version: 802.16m (2011)
  Functions in 2-11 or 11-66 GHz range
  Licensed or nonlicensed frequencies
Ability to transmit and receive signals up to 30 miles
  With fixed antennas
  About 10 miles when antennas are mobile

## Slide 59: 802.16 (WiMAX) (cont’d.)
802.16m
  Positioned to compete favorably with cellular data services
  Backwards compatible with 802.16e equipment
Maximum throughput
  Downlink: 120Mbps
  Uplink: 60Mbps
  Future improvements could take to 1Gbps

## Slide 60
Figure 8-19 WiMAX network
Courtesy Course Technology/Cengage Learning

## Slide 61
Figure 8-20 WiMAX residential antenna
Courtesy of Laird Technologies

## Slide 62: Cellular
Initially designed for analog telephone service
  Today deliver data and voice
Cellular technology generations
  1G: analog
  2G: digital transmission up to 240Kbps
  3G: data rates up to 384Kbps
    Data communications use packet switching
  4G: all-IP, packet switched network for data and voice

## Slide 63: Cellular (cont’d.)
Network infrastructure
  Cells served by antenna and base station
  Controller assigns mobile clients frequencies
Cell size depends on:
  Network’s access method
  Region topology
  Population
  Amount of cellular traffic

## Slide 64
Figure 8-22 Cellular network
Courtesy Course Technology/Cengage Learning

## Slide 65: Cellular (cont’d.)
Basic infrastructure
  HSPA+ (High Speed Packet Access Plus)
    3G technology
  LTE (Long Term Evolution)
    4G technology
Table 8-2 Characteristics of some wireless WAN services
Courtesy Course Technology/Cengage Learning

## Slide 66: Satellite
Used to deliver:
  Digital television and radio signals
  Voice and video signals
  Cellular and paging signals
  Data services to mobile clients in remote locations
Most popular satellite orbit
  Geosynchronous Earth orbit (GEO)
    Satellites orbit at same rate Earth turns

## Slide 67: Satellite (cont’d.)
Downlink
  Satellite transponder transmits signal to Earth-based receiver
Typical satellite
  24 to 32 transponders
  Unique downlink frequencies

## Slide 68: Satellite (cont’d.)
Satellite frequency bands
  L-band—1.5–2.7 GHz
  S-band—2.7–3.5 GHz
  C-band—3.4–6.7 GHz
  Ku-band—12–18 GHz
  Ka-band—18–40 GHz
Within bands
  Uplink, downlink transmissions differ

## Slide 69: Satellite (cont’d.)
Satellite Internet services
  Subscriber uses small satellite dish antenna, receiver
  Exchanges signals with provider’s satellite network
  Typically asymmetrical
  Bandwidth shared among many subscribers
  Throughput controlled by service provider
  Slower, more latency than other wireless WAN options

## Slide 70
Figure 8-23 Satellite communication
Courtesy Course Technology/Cengage Learning

## Slide 71: Summary
Wireless spectrum used for data and voice communications
  Each type of service associated with specific frequency band
Wireless communication: fixed or mobile
Standards vary by frequency, signal method, and range
  Notable wireless standards include 802.11 a/b/g/n
WiMAX 2: specified in IEEE’s 802.16m standard
Satellites can provide wireless data services