## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 13
Troubleshooting Network Problems

## Slide 2: Objectives
Describe the steps involved in an effective troubleshooting methodology
Follow a systematic troubleshooting process to identify and resolve networking problems
Document symptoms, solutions, and results when troubleshooting network problems
Use a variety of software and hardware tools to diagnose problems

## Slide 3: Troubleshooting Methodology
Proceed logically and methodically
Follow recommended steps
Use experience when necessary
Logical approach benefits
  Prevents wasteful, time-consuming efforts
    Unnecessary software, hardware replacements

## Slide 4: Troubleshooting Methodology (cont’d.)
Troubleshooting steps
  Identify problem
    Gather information
    Identify symptoms
    Question users
    Determine if anything has changed
  Establish theory of probable cause
    Question the obvious

## Slide 5: Troubleshooting Methodology (cont’d.)
Troubleshooting steps (cont’d.)
  Test theory to determine cause
    If theory confirmed, determine next steps
    If theory not confirmed, establish new theory or escalate
  Establish action plan
  Implement solution or escalate
  Verify full functionality
  Implement preventative measures if applicable
  Document findings, actions, outcomes

## Slide 6: Identify the Problem and Its Symptoms
Ask questions
  Answers help identify network problem symptoms
Avoid jumping to conclusions about symptoms
Pay attention to:
  Users
  System and network behaviors
  Error messages
Treat each symptom uniquely

## Slide 7: Identify the Problem and Its Symptoms (cont’d.)
Determine the problem’s scope
  Find out how many users or network segments are affected
  Narrow down time frame during which problem occurred
Benefits of narrowing scope
  Eliminate causes, point to others

## Slide 8: Identify the Problem and Its Symptoms (cont’d.)
Take time to troubleshoot correctly
  Ask specific questions
  Filter unrelated user information
Discover time and frequency of problem
  May reveal more subtle network problems
Identify affected problem area
  Leads to next troubleshooting steps

## Slide 9
Figure 13-1 Identifying the area affected by a problem
Courtesy Course Technology/Cengage Learning

## Slide 10
Figure 13-2 Identifying the chronological scope of a problem
Courtesy Course Technology/Cengage Learning

## Slide 11: Identify the Problem and Its Symptoms (cont’d.)
Question users
  Ensure human error is not source of problem
  Watch the user if possible
    Use remote desktop software
    Ask what appears on the screen
    Use methodical approach
Determine if anything has changed
  Be aware of recent network changes
  Ask questions pinpointing problem resulting from network change

## Slide 12: Identify the Problem and Its Symptoms (cont’d.)
Possible actions if network change created problem
  Correct problem
    Sometimes the best solution
  Reverse change
    Less risky, less time consuming
Network change records
  Track what has changed
  Make records available to staff members

## Slide 13: Establish a Theory of Probable Cause
Re-create the symptoms
  Follow same steps as person reporting symptom
Verify Physical layer connectivity
  Cabling and network adapters a common source of problems
  Symptoms of physical layer problems
    Segment, network lengths exceed standards
    Noise
    Improper terminations, faulty, loose, or poorly crimped connectors
    Damaged cables
    Faulty NICs, GBICs, SFPs

## Slide 14: Establish a Theory of Probable Cause
Verify Physical layer connectivity (cont’d.)
  Diagnosing Physical layer problems
    Ask questions
    Verify connections between devices
    Verify soundness of connection hardware
Verify logical connectivity
  Consider error messages
  Note changes in operating system or applications
  Determine if the problem is repeatable
  Find out who is affected by the problem
  Narrow down possibilities

## Slide 15
Figure 13-3 Verifying physical connectivity
Courtesy Course Technology/Cengage Learning

## Slide 16: Test the Theory to Determine Cause
Test Physical layer theories
  Complicated problems require effort and analysis
Example approaches
  Use a cable testing tool
  Check to make sure NIC is seated firmly in slot
  Use wireless analyzer
  Follow cables to verify physical connectivity
  Exchange suspect component with a known good one
  Try different port, data jack, or SFP module

## Slide 17: Test the Theory to Determine Cause (cont’d.)
Test logical connectivity theories
  Testing theory may end up solving the problem
Example approaches
  View switch configuration to determine which nodes are included in VLANs
  Investigate user permissions
  Examine NIC configuration
  Ensure routing table includes valid entries
  Use tools such as ping, netstat, route, traceroute
  Check wireless client settings

## Slide 18: Test the Theory to Determine Cause (cont’d.)
Escalate if necessary
  Ask colleague with more experience or knowledge
Help desk analysts
  Proficient in basic workstation, network troubleshooting
  First-level support
Network specialist
  Second-level support
Help desk coordinator
  Third-level support personnel
Follow escalation procedures

## Slide 19: Establish a Plan of Action to Resolve the Problem
Consider how solution affects users, network functionality
Scope
  Assess solution’s scope before implementing
  Wait if not an emergency
Trade-offs
  Solution may restore functionality for one user group
    But may remove functionality for others

## Slide 20: Establish a Plan of Action to Resolve the Problem (cont’d.)
Security
  Be aware of security implications
    Inadvertent removal of network access, resource privileges
  Before upgrade, patch installation
    Understand access changes for authorized, unauthorized users

## Slide 21: Establish a Plan of Action to Resolve the Problem (cont’d.)
Scalability of solution
  Position network for future additions, enhancements
  Temporary fix organization will outgrow
Cost
  Weigh options carefully
  Consider addressing poor network performance areas separately

## Slide 22: Establish a Plan of Action to Resolve the Problem (cont’d.)
Use vendor information
  Manufacturer documentation
  Free online troubleshooting information
    Searchable databases
    Sophisticated web interfaces for troubleshooting equipment
    Vendor’s technical phone support
  Consult with others within, outside your organization

## Slide 23: Implement the Solution or Escalate as Necessary
Solution implementation
  Time required may be minimal or long
  Requires foresight, patience
  Use methodical and logical approach
    Leads to efficient correction process
  Problem causing catastrophic outages should be solved as quickly as possible
  Follow series of steps
    Implement a safe, reliable solution
Large-scale fixes
  Roll out changes in stages

## Slide 24: Verify Full System Functionality
Verify problem solution is complete
  Type of testing depends on solution
    Also area affected by problem
  May not be able to test solution immediately
Determine how and why solution is successful
Evaluate effects on users and functionality
Consider how similar problems may be prevented in the future

## Slide 25: Document Findings, Actions, and Outcomes
Necessary to record:
  Problem symptoms and cause(s)
  Solution(s)
Justification for recording
  Impossible to remember each incident’s circumstances
  Job changes
Use centrally located database
  Accessible to all networking personnel

## Slide 26: Document Findings, Actions, and Outcomes (cont’d.)
Call tracking system (help desk software)
  User-friendly, graphical
  Prompts for problem information
  Assigns unique problem number
  Highly customizable
  If not available, use simple electronic form
Supported services list document
  Lists all supported service, software and contacts
Follow-up with user who reported problem

## Slide 27: Document Findings, Actions, and Outcomes (cont’d.)
Notify others of changes
  Record resolution in call tracking system
  Alert others about problem, solution
  Notify others of network changes made
Change management system
  Process or program
  Means of documenting network changes
Minor modifications need not be recorded
  Example: user password reset

## Slide 28: Troubleshooting Tools
Utilities help troubleshoot network problems
  Ping
  Specialized tools
    Specifically designed to analyze, isolate network problems
    Simple continuity testers
    Protocol analyzers
Tool selection dependencies
  Problem being investigated
  Network characteristics

## Slide 29: Tone Generator and Tone Locator
Ideal situation
  Telecommunications closet ports, wire terminations labeled properly
Reality
  Telecommunications closet disorganized, poorly documented
Tone generator (toner)
  Small electronic device
  Issues signal on wire pair

## Slide 30: Tone Generator and Tone Locator (cont’d.)
Tone locator (probe)
  Emits tone when electrical activity detected
Probe kit
  Generator and locator combination
Testing requires trial and error
Used to determine where wire pair terminates
Not used to determine cable characteristics

## Slide 31
Figure 13-4 Use of a tone generator and tone locator
Courtesy Course Technology/Cengage Learning

## Slide 32: Multimeter
Specialized tools used to test cables for faults
  Isolate problems with network cables
Multimeter
  Measures electric circuit characteristics
    Resistance and voltage
Voltmeter
  Measures voltage of an electric current
    Voltage creates signals over network wire

## Slide 33: Multimeter (cont’d.)
Resistance
  Fundamental wire property
  Depends on wire’s molecular structure, size
  Measured in ohms using ohmmeter
Impedance
  Resistance contributing to controlling signal
  Measured in ohms
  Telltale factor for ascertaining where cable faults lie
  Some required for proper signal transmission and interpretation

## Slide 34: Multimeter (cont’d.)
Multimeter
  Single instrument for measuring impedance, resistance, voltage on a wire
  Has several uses
  Sophistication, features, and costs vary

## Slide 35
Figure 13-5 A multimeter
Courtesy Fluke Networks

## Slide 36: Cable Continuity Testers
Cable checkers (continuity testers, cable testers)
  Tests whether cable carries signal to destination
Copper-based cable tester
  Consists of two parts
    Base unit generates voltage
    Remote unit detects voltage
Series of lights, audible tone
  Used to signal pass/fail

## Slide 37: Cable Continuity Testers (cont’d.)
Some continuity testers verify UTP, STP wires paired correctly
  Not shorted, exposed, crossed
Fiber optic continuity tester
  Issues light pulses on fiber
  Determines whether pulses reach other end
Test all cables to ensure meeting network’s required standards
  Homemade or purchased
Offer convenience: portable, lightweight, low cost

## Slide 38
Figure 13-6 Cable continuity tester
Courtesy Fluke Networks

## Slide 39: Cable Performance Testers
Determines if cable carrying current
Continuity testers versus performance testers
  Differ in sophistication and price
  Performance tester accomplishes same tests
    Can also perform additional tasks
TDR (time domain reflectometer)
  Included with sophisticated performance testers
  Issue signal, measures signal bounce back
  Indicates distance between nodes
  Indicates whether terminators properly installed, functional

## Slide 40: Cable Performance Testers (cont’d.)
Fiber-optic connections testers
  Use OTDRs (optical time domain reflectometers)
  Transmit light-based signals of different wavelengths over fiber
OTDRs
  Measure fiber length
  Determine faulty splice locations, breaks, connectors, bends
  Measure attenuation over cable
  Expensive

## Slide 41
Figure 13-7 A high-end cable performance tester
Courtesy Fluke Networks

## Slide 42: Voltage Event Recorders
Voltage event
  Any condition where voltage exceeds or drops below predefined levels
Voltage event recorder
  Collects data about power quality
  Downloads data to workstation
    Analyzed by software
  Cost: up to $5000

## Slide 43
Figure 13-8 Voltage event recorder
Courtesy Fluke Networks

## Slide 44: Butt Set
Lineman’s handset, telephone test set
  Butt into telephone conversation
  Rugged, sophisticated telephone
Uses
  Determine if line functioning (detects dial tone)
  Receives signal
  Picks up noise affecting signal
Sophisticated butt sets
  Perform rudimentary cable testing

## Slide 45
Figure 13-9 Butt set
Courtesy Fluke Networks

## Slide 46: Network Monitors
Software-based tool
  Continually monitors network traffic from server, workstation attached to network
  Interprets up to Layer 3
  Determines protocols passed by each frame
  Cannot interpret frame data
Included in NOS
  Microsoft’s Network Monitor
Tools developed by other software companies
  Purchase or free download

## Slide 47: Network Monitors (cont’d.)
Network adapter
  Must support promiscuous mode
Common terms for abnormal data patterns, packets
  Local collisions
  Late collisions
  Runts
  Giants
  Jabber
  Negative frame sequence checks
  Ghosts

## Slide 48: Protocol Analyzers
Protocol analyzer (network analyzer)
  Captures traffic, analyzes frames
    Typically to Layer 7
Variety of protocol analyzer software available
  Wireshark
Same features as network monitor
  Includes additional features
  Generates traffic to reproduce network problem
Sniffer (packet sniffer)
  Older term referring to hardware device

## Slide 49
Figure 13-10 Traffic captured by a protocol analyzer
Courtesy Fluke Networks

## Slide 50: Protocol Analyzers (cont’d.)
Offers versatility in information type, depth
  Can collect more information than can be reasonably processed
  Set filters on gathered data
Before using network monitor or protocol analyzer:
  Learn what network traffic normally looks like
  Capture data for time period on regular basis
    Establish a baseline to compare with future analyses

## Slide 51: Wireless Network Testers
Tools containing wireless NICs, running wireless protocols
Workstation wireless network connection properties
  Shows little about wireless environment
    Connection duration, signal speed and strength, number of packets exchanged
  Only applies to one workstation
Programs scan for wireless signals
  Discover access points, wireless stations transmitting

## Slide 52: Wireless Network Testers (cont’d.)
Spectrum analyzer
  Tool to assess wireless signal quality
Hardware instruments for wireless network testing
  Typically more portable than workstation with software tools
  Preinstalled with network analysis tools
  Accessible from simple, graphical interface
  Contain powerful antennas

## Slide 53
Figure 13-11 Wireless network testing tool
Courtesy Fluke Networks

## Slide 54: Summary
Methodical, logical troubleshooting methodology
  Key to solving network problems
Troubleshooting tools
  Tone generator, tone locator
  Multimeters
  Cable continuity testers
  Cable performance tester
  Voltage event recorder
  Butt set
  Network monitors and protocol analyzers
  Wireless network testing tools