## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 14
Ensuring Integrity and Availability

## Slide 2: Objectives
Identify the characteristics of a network that keep data safe from loss or damage
Protect an enterprise-wide network from malware
Explain fault-tolerance techniques for storage, network design, connectivity devices, naming and addressing services, and servers
Discuss best practices for network backup and recovery
Describe the components of a useful disaster recovery plan and the options for disaster contingencies

## Slide 3: What Are Integrity and Availability?
Integrity
  Soundness of network’s programs, data, services, devices, connections
Availability
  How consistently and reliably a file or system can be accessed
Uptime
  Measure of time functioning normally between failures
  Often expressed as percent uptime

## Slide 4
Table 14-1 Availability and downtime equivalents
Courtesy Course Technology/Cengage Learning

## Slide 5: What Are Integrity and Availability? (cont’d.)
Integrity and availability compromised by:
  Security breaches
  Natural disasters
  Malicious intruders
  Power flaws
  Human error
Follow guidelines to keep network highly available
  See Pages 646-647 of text

## Slide 6: Malware
Malicious software
Program designed to intrude upon or harm system, resources
  Examples: viruses, Trojan horses, worms, bots
Virus
  Replicating program intent to infect more computers
  Copied to system without user knowledge
  Replicates through network connections or exchange of external storage devices

## Slide 7: Malware (cont’d.)
Trojan horse (Trojan)
  Program that disguises itself as something useful
    Actually harms your system

## Slide 8: Malware Types and Characteristics
Malware categorized by location and propagation method
  Boot sector viruses
  Macro viruses
  File-infector viruses
  Worms
  Trojan horses
  Network viruses
  Bots

## Slide 9: Malware Types and Characteristics (cont’d.)
Malware characteristics
  Encryption
    Some viruses, worms, Trojan horses
  Stealth
    Hidden to prevent detection
    Disguised as legitimate programs
  Polymorphism
    Change characteristics every time they transfer to new system
    Use complicated algorithms; incorporate nonsensical commands

## Slide 10: Malware Types and Characteristics (cont’d.)
Malware characteristics (cont’d.)
  Time dependence
    Programmed to activate on particular date
    Can remain dormant and harmless until date arrives
    Logic bombs: programs designed to start when certain conditions met
Malware can exhibit more than one characteristic

## Slide 11: Malware Protection
Effective malware protection requires:
  Choosing appropriate anti-malware program
  Monitoring network
  Continually updating anti-malware program
  Educating users

## Slide 12: Malware Protection (cont’d.)
Malware leaves evidence
  Some detectable only by anti-malware software
  User symptoms
    Unexplained file size increases
    Significant, unexplained system performance decline
    Unusual error messages
    Significant, unexpected system memory loss
    Periodic, unexpected rebooting
    Display quality fluctuations
Malware often discovered after damage done

## Slide 13: Malware Protection (cont’d.)
Anti-malware key software functions
  Signature scanning
    Compares file’s content with known malware signatures
  Integrity checking
    Compares current file characteristics against archived version
  Monitoring unexpected file changes
  Receive regular updates from central network console
  Consistently report valid instances of malware

## Slide 14: Malware Protection (cont’d.)
Anti-malware software implementation
  Dependent upon environment’s needs
Key: deciding where to install software
  Desktop machines
  Server
Balance protection with performance impact

## Slide 15: Malware Protection (cont’d.)
Anti-malware policies
  Rules for using anti-malware software
  Rules for installing programs, sharing files, using external disks
Management should authorize and support policy
Anti-malware policy guidelines
  See Pages 651-652 of text
Measures designed to protect network from damage, downtime

## Slide 16: Fault Tolerance
Capacity for system to continue performing
  Despite unexpected hardware, software malfunction
Failure
  Deviation from specified system performance level
    Given time period
Fault
  Malfunction of one system component
  Can result in failure
Fault-tolerant system goal
  Prevent faults from progressing to failures

## Slide 17: Fault Tolerance (cont’d.)
Degrees of fault tolerance
  Optimal level depends on file or service criticality
  Highest level
    System remains unaffected by most drastic problem

## Slide 18: Environment
Consider network device environment
Protect devices from:
  Excessive heat, moisture
    Use temperature, humidity monitors
  Break-ins
  Natural disasters

## Slide 19: Power
Blackout
  Complete power loss
Brownout
  Temporary dimming of lights
Causes
  Forces of nature
  Utility company maintenance, construction
Solution
  Alternate power sources

## Slide 20: Power (cont’d.)
Power flaws not tolerated by networks
Types of power flaws that create damage
  Surge
    Momentary increase in voltage
  Noise
    Fluctuation in voltage levels
  Brownout
    Momentary voltage decrease
  Blackout
    Complete power loss

## Slide 21: Power (cont’d.)
Uninterruptible power supplies (UPSs)
  Battery-operated power source
  Directly attached to one or more devices
  Attached to a power supply
  Prevents harm to device, service interruption
UPS categories
  Standby
  Online

## Slide 22: Power (cont’d.)
Standby UPS (offline UPS)
  Provides continuous voltage
  Switches instantaneously to battery upon power loss
  Restores power
  Problems
    Time to detect power loss
    Device may have shut down or restarted

## Slide 23: Power (cont’d.)
Online UPS
  A/C power continuously charges battery
  No momentary service loss risk
  Handles noise, surges, sags
    Before power reaches attached device
  More expensive than standby UPSs
Factors to consider when choosing UPS
  Amount of power needed
  Period of time to keep device running
  Line conditioning
  Cost

## Slide 24
Figure 14-1 Standby and online UPSs
Courtesy of Schneider Electric

## Slide 25: Power (cont’d.)
Generators
  Powered by diesel, liquid propane, gas, natural gas, or steam
  Do not provide surge protection
  Provide electricity free from noise
  Used in highly available environments
Generator choice
  Calculate organization’s crucial electrical demands
  Determine generator’s optimal size

## Slide 26
Figure 14-2 UPSs and a generator in a network design
Courtesy Course Technology/Cengage Learning

## Slide 27: Network Design
Supply multiple paths for data travel
Topology
  LAN: star topology and parallel backbone provide greatest fault tolerance
  WAN: full-mesh topology
  SONET technology
    Uses two fiber rings for every connection
    Can easily recover from fault in one of its links

## Slide 28
Figure 14-3 Full-mesh WAN
Courtesy Course Technology/Cengage Learning

## Slide 29: Network Design (cont’d.)
Review PayNTime example on Pages 657-658
Possible solutions: supply duplicate connection
  Use different service carriers
  Use two different routes
    Critical data transactions follow more than one path
Network redundancy advantages
  Reduces network fault risk
    Lost functionality, profits
Disadvantage: cost

## Slide 30: Network Design (cont’d.)
Scenario: two critical links
  Capacity, scalability concerns
  Solution
    Partner with ISP
    Establish secure VPNs
  See Figure 14-4

## Slide 31
Figure 14-4 VPNs linking multiple customers
Courtesy Course Technology/Cengage Learning

## Slide 32: Network Design (cont’d.)
Scenario
  Devices connect one LAN, WAN segment to another
    Experience a fault
  VPN agreement with national ISP
    Single T1 link supports five customers
Figure 14-5 Single T1 connectivity
Courtesy Course Technology/Cengage Learning

## Slide 33: Network Design (cont’d.)
Problem with arrangement of Figure 14-5
  Many single points of failure
    T1 link failure
    Firewall, router, CSU/DSU, multiplexer, or switch
Solution
  Redundant devices with automatic failover
  Hot swappable devices
    Immediately assume identical component duties
Cold spare
  Duplicate device on hand, not installed

## Slide 34
Figure 14-6 Fully redundant T1 connectivity
Courtesy Course Technology/Cengage Learning

## Slide 35: Network Design (cont’d.)
Failover capable or hot swappable components
  Desired for switches or routers supporting critical links
  Adds to device cost
Link aggregation (bonding)
  Combination of multiple network interfaces to act as one logical interface
  Example: NIC teaming
Load balancing
  Automatic traffic distribution over multiple components or links

## Slide 36
Figure 14-7 Link aggregation between a switch and server
Courtesy Course Technology/Cengage Learning

## Slide 37: Network Design (cont’d.)
Naming and addressing services
  Failure causes nearly all traffic to come to a halt
Solution: maintain redundant name servers
DNS caching servers
  Allows local name resolution
  Faster performance
  Reduces burden on master name server

## Slide 38
Figure 14-8 Redundant name servers
Courtesy Course Technology/Cengage Learning

## Slide 39: Network Design (cont’d.)
DNS can point to redundant locations for each host name
  Use different IP addresses that all point to identical Web servers
Round-robin DNS
  Use each IP address sequentially
Load balancer
  Dedicated device for intelligent traffic distribution
  Considers traffic levels when forwarding requests

## Slide 40
Figure 14-9 Redundant entries in a DNS zone file
Courtesy Course Technology/Cengage Learning

## Slide 41: Network Design (cont’d.)
CARP (Common Address Redundancy Protocol)
  Allows pool of computers to share IP addresses
  Master computer receives request
    Parcels out request to one of several group computers

## Slide 42
Figure 14-10 Round-robin DNS with CARP
Courtesy Course Technology/Cengage Learning

## Slide 43: Servers
Critical servers
  Contain redundant components
    Provide fault tolerance, load balancing
Server mirroring
  Fault-tolerance technique
  One device, component duplicates another's activities
  Uses identical servers, components
  High-speed link between servers
  Synchronization software
  Form of replication
    Dynamic copying of data from one location to another

## Slide 44: Servers (cont’d.)
Server mirroring advantage
  Flexibility in server location
Disadvantages
  Time delay for mirrored server to assume functionality
  Toll on network as data copied between sites
Hardware and software costs
  May be justifiable

## Slide 45: Servers (cont’d.)
Clustering
  Links multiple servers together
    Act as single server
Clustered servers share processing duties
  Appear as single server to users
Failure of one server
  Others take over
  More cost-effective than mirroring
  For large networks

## Slide 46: Servers (cont’d.)
Clustering advantages over mirroring
  Each clustered server
    Performs data processing
    Always ready to take over
  Reduces ownership costs
  Improves performance

## Slide 47: Storage
Data storage
  Issues of availability and fault tolerance apply
Various methods available
  Ensure shared data and applications never lost or irretrievable
RAID (Redundant Array of Independent [or Inexpensive] Disks)
  Collection of disks
  Provide shared data, application fault tolerance

## Slide 48: Storage (cont’d.)
Disk array (drive)
  Group of hard disks
RAID drive (RAID array)
  Collection of disks working in a RAID configuration
  Single logical drive

## Slide 49: Storage (cont’d.)
Hardware RAID
  Set of disks, separate disk controller
  RAID array managed exclusively by RAID disk controller
    Attached to server through server’s controller interface
Software RAID
  Software implements and controls RAID techniques
  Any hard disk type
  Less expensive (no controller, disk array)
  Performance rivals hardware RAID
Several different types of RAID available

## Slide 50: Storage (cont’d.)
NAS (Network Attached Storage)
  Specialized storage device, storage device group
  Provides centralized fault-tolerant data storage
Difference from RAID
  Maintains own interface to LAN
Advantages
  NAS device contains own file system
    Optimized for saving, serving files
  Easily expandable
  No service interruption

## Slide 51
Figure 14-11 Network attached storage on a LAN
Courtesy Course Technology/Cengage Learning

## Slide 52: Storage (cont’d.)
Disadvantage
  No direct communication with network clients
NAS use
  Enterprises requiring fault tolerance, fast data access
SANs (Storage Area Networks)
  Distinct networks of storage devices
  Communicate directly with each other, other networks
Typical SAN contains multiple storage devices
  Connected to multiple, identical servers

## Slide 53: Storage (cont’d.)
SAN advantages
  Fault tolerant
  Extremely fast
    Special transmission method
    Fiber-optic media, proprietary protocols
    Example: Fibre Channel
  Install in location separate from LAN served
    Provides added fault tolerance
  Highly scalable
  Faster, more efficient method of writing data

## Slide 54: Storage (cont’d.)
SAN disadvantages
  High cost
    Small SAN: $100,000
    Large SAN: several million dollars
  More complex than NAS, RAID
    Training, administration efforts required
Use
  Environments with huge data quantities requiring quick availability

## Slide 55
Figure 14-12 A storage area network
Courtesy Course Technology/Cengage Learning

## Slide 56: Data Backup
Backup
  Copies of data or program files
  Created for archiving, safekeeping
  Store off site
Without backup: risk losing everything
Many backup options available
  Performed by different software and hardware
  Use different storage media types
Can be controlled by NOS utilities, third-party software

## Slide 57: Backup Media and Methods
Approach to selecting backup media, methods
  Ask questions to select appropriate solution
Optical media
  Media storing digitized data
  Uses laser to write data, read data
  Examples: CDs, DVDs
Backup requirements
  Recordable CD or DVD drive, software utility
Blu-ray
  Optical storage format

## Slide 58: Backup Media and Methods (cont’d.)
DVD and Blu-ray DVD disadvantages
  Writing data takes longer than other media
  Requires more human intervention than other backup methods
Tape backups
  Copying data to magnetic tape
Requirements
  Tape drive connected to network
  Management software
  Backup media

## Slide 59: Backup Media and Methods (cont’d.)
Small network tape backups
  Stand-alone tape drives attached to each server
Large network tape backups
  One large, centralized tape backup device
    Manages all subsystems’ backups
Extremely large environments
  Robots retrieve, circulate tapes from tape storage library

## Slide 60: Backup Media and Methods (cont’d.)
External disk drives (removable disk drives)
  Storage device attached temporarily to computer
    USB, PCMCIA, FireWire, CompactFlash port
  Simple to use, save, share data
  Temporary drive appears like any other drive
Large data amount requirements
  Backup control features, higher storage capacity, faster read-write access

## Slide 61: Backup Media and Methods (cont’d.)
Network backups
  Save data to another place on network
  Different server, another WAN location
  SAN, NAS storage device
Online backup (cloud backup)
  Saves data to another company’s storage array using Internet
  Implement strict security measures
  Automated backup, restoration processes
Evaluate online back up provider
  Test speed, accuracy, security, recovery

## Slide 62: Backup Strategy
Devise a strategy to perform reliable backups
Document in accessible area
Address various questions
Archive bit
  File attribute
    Set to on or off
    On indicates file must be archived
  Used by various backup methods

## Slide 63: Backup Strategy (cont’d.)
Full backup
  All data copied
  Uncheck archive bits
Incremental backup
  Copy data changed since last full, incremental backup
  Uncheck archive bits
Differential backup
  Copy only data changed since last backup
  All data marked for subsequent backup
  Does not uncheck archive bits

## Slide 64: Backup Strategy (cont’d.)
Determine best backup rotation scheme
  Plan specifies when and how often backups occur
  Goal
    Provide excellent data reliability without overtaxing network, requiring intervention
Grandfather-Father-Son strategy
  Uses backup sets
    Daily (son)
    Weekly (father)
    Monthly (grandfather)

## Slide 65
Figure 14-13 The Grandfather-Father-Son backup rotation scheme
Courtesy Course Technology/Cengage Learning

## Slide 66: Backup Strategy (cont’d.)
Ensure backup activity recorded in backup log
  Backup date
  Media identification
  Type of data backed up
  Type of backup
  Files backed up
  Backup location
Establish regular verification schedule
  Attempt to recover files periodically

## Slide 67: Disaster Recovery
Disaster recovery
  Restoring critical functionality, data
    After enterprise-wide outage
    Affecting more than single system, limited group
Consider possible extremes
  Not relatively minor outages, failures, security breaches, data corruption

## Slide 68: Disaster Recovery Planning
Account for worst-case scenarios
Identify disaster recovery team
Provide contingency plans
  Restore and replace:
    Computer systems
    Power
    Telephony systems
    Paper-based files
Plan contains various sections
Lessen critical data loss risk

## Slide 69: Disaster Recovery Contingencies
Cold site
  Components necessary to rebuild network exist
  Not appropriately configured, updated, or connected
Warm site
  Components necessary to rebuild network exist
  Some appropriately configured, updated, and connected
Hot site
  Components exist and match network’s current state
  All appropriately configured, updated, and connected

## Slide 70: Summary
Integrity and availability: important concepts
Malware aims to intrude upon or harm system
Anti-malware software part of network protection
Fault tolerance allows system to continue performing despite unexpected malfunction
Various types of backup power supplies exist
Network design can provide different levels of fault tolerance
Mirroring, clustering, RAID, NAS, and SAN can provide fault tolerance