## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 15
Network Management

## Slide 2: Objectives
Explain basic concepts related to network management
Discuss the importance of documentation, baseline measurements, policies, and regulations in assessing and maintaining a network’s health
Manage a network’s performance using SNMP-based network management software, system and event logs, and traffic-shaping techniques

## Slide 3: Objectives (cont’d.)
Identify the reasons for and elements of an asset management system
Plan and follow regular hardware and software maintenance routines

## Slide 4: Fundamentals of Network Management
Network management
  Assess, monitor, and maintain all network aspects
  Scope differs according to network’s size and importance
  Several network management disciplines
  All share same goals
    Enhance efficiency and performance
    Prevent costly downtime and loss
  Predict problems before they occur

## Slide 5: Documentation
Network aspects to document
  Physical topology
  Access method
  Protocols
  Devices
  Operating systems
  Applications
  Configurations

## Slide 6: Documentation (cont’d.)
Configuration management
  Collection, storage, assessment of configuration documentation
Documenting all network aspects
  Saves future work
Network diagrams
  Graphical representations of network’s devices, connections
  Use popular Cisco icons
  Provide broad snapshot of network’s physical or logical topology

## Slide 7
Figure 15-1 Network diagram using Cisco symbols
Courtesy Course Technology/Cengage Learning

## Slide 8: Documentation (cont’d.)
Wiring schematic
  Graphical representation of network’s wired infrastructure
  Detailed form
    Includes every wire connecting network devices
  Less detailed form
    Single line represents group of wires connecting several clients to a switch

## Slide 9
Figure 15-2 Wiring schematic
Courtesy Course Technology/Cengage Learning

## Slide 10: Baseline Measurements
Baseline
  Report of network’s current operation state
Example baseline measurements
  Network backbone utilization rate
  Number of users logged on per day or per hour
  Number of protocols running on network
  Error statistics
    Runts, collisions, jabbers, giants
  Frequency of application use
  Bandwidth usage

## Slide 11
Figure 15-3 Baseline of daily network traffic
Courtesy Course Technology/Cengage Learning

## Slide 12: Baseline Measurements (cont’d.)
Compare future and past performance
  Most critical network, user functions
  More data provides more accuracy
Forecasting network traffic patterns
  Difficult to predict users’ habits, new technology effects, changes in resource demand
Gathering baseline data
  Software applications
    Freeware
    Expensive, customizable hardware and software
  Determine use before selecting

## Slide 13: Policies, Procedures, and Regulations
Rules limit chaos, confusion, downtime
Sound network management policies
  Media installation and management
  Network addressing policies
  Security-related policies
  Troubleshooting procedures
  Backup and disaster recovery procedures

## Slide 14: Policies, Procedures, and Regulations (cont’d.)
State and federal regulations
  CALEA (Communications Assistance for Law Enforcement Act)
    Telecommunications carriers, equipment manufacturers must provide for surveillance capabilities
  HIPAA (Health Insurance Portability and Accountability Act)
    Protect medical records security and privacy
Many policies and procedures
  Not laws
  Best practices to prevent network problems

## Slide 15: Fault and Performance Management
Assess network’s status on an ongoing basis
Performance management
  Monitor links and devices’ ability to keep up with demand
Fault management
  Detection and signaling of device, link, component faults

## Slide 16: Network Management Systems
Enterprise-wide network management systems
  Accomplish fault and performance management
  All use similar architecture
  Polling
    Collecting data from multiple networked devices at regular intervals
  Agent
    Software routine
    Collects information about device’s operation
    Provides information to network management application

## Slide 17: Network Management Software (cont’d.)
Various aspects of a device can be managed
  Processor, memory, hard disk, NIC, and intangibles
MIB (Management Information Base)
  Contains managed devices definition, data
SNMP (Simple Network Management Protocol)
  Used to communicate managed device information
  Part of TCP/IP suite
  SNMPv3: most secure version of the protocol
  SNMPv2 still widely used

## Slide 18
Figure 15-4 Network management architecture
Courtesy Course Technology/Cengage Learning

## Slide 19: Network Management Software (cont’d.)
Several ways to view and analyze data
Network management applications
  Flexible
  Challenging to configure and fine-tune
  Choose correct type and amount of information to collect
Faults can trigger alarms
  Also recorded in system and event logs

## Slide 20
Figure 15-5 Map showing network status
Courtesy Course Technology/Cengage Learning

## Slide 21: System and Event Logs
Log
  Contains recorded conditions recognized by operating system
Event log
  Windows-based computer log containing monitored device information
Event Viewer application
  Application to view log information in Windows

## Slide 22
Figure 15-6 Event log on a workstation running Windows 7
Courtesy Course Technology/Cengage Learning

## Slide 23: System and Event Logs (cont’d.)
Syslog function
  Standard for generating, storing, and processing messages about events on Linux or UNIX
  Data written to system log
Using logs for fault management
  Logs keep history
  Information collected does not point to problem
  Logs must be monitored for errors
  Application used for viewing, filtering information

## Slide 24: Traffic Shaping
Traffic shaping
  Manipulating packet, data stream, and connection characteristics
    Manage type and amount of traffic traversing network
  Goals
    Assure timely delivery of most important traffic
    Offer best possible performance for all users

## Slide 25: Traffic Shaping (cont’d.)
Techniques
  Delay less important traffic
  Increase priority of more important traffic
  Traffic policing
    Limit traffic volume flowing in and out of interface during specified time period
    Limit momentary throughput rate for an interface
Not without controversy
  Comcast discriminated against certain traffic types

## Slide 26
Figure 15-7 Traffic volume before and after applying limits
Courtesy Course Technology/Cengage Learning

## Slide 27: Traffic Shaping (cont’d.)
Traffic prioritization
  Treating more important traffic preferentially
Prioritization based on characteristics
  Protocol
  IP address
  User group
  DiffServ (Differentiated Services) flag or TOS (type of service) field in IP datagram
  VLAN tag in Data Link layer frame
  Service or application

## Slide 28: Caching
Caching
  Local storage of frequently needed files
  Allows quick access
Web caching
  Most common caching type, highly customizable
  Web pages stored locally
    On host or network, and then delivered to requesters
ISP cache engine
  Network device devoted to storage, frequently requested file delivery
  Saves money; lowers WAN traffic

## Slide 29: Asset Management
Identifying and tracking hardware and software
First step
  Inventory each network node
Organization needs
  Determine appropriate asset management tool
Benefits
  Simplifies maintaining and upgrading network
  Provides information about hardware and software costs and benefits

## Slide 30: Change Management
Managing change while maintaining network efficiency and availability:
  Requires good planning
Common software and hardware changes
  Range from installing patches to replacing network backbone
Several ways to approach changes

## Slide 31: Software Changes
Software upgrades
  Important for keeping system running optimally
Application patches and upgrades
  Correction, improvements, and enhancements to particular software application
  Change only part of an application
General steps
  Determine whether patch or upgrade is necessary
  Research change purpose, compatibility, and effects
  Determine whether changes should apply to all users
  Determine distribution method

## Slide 32: Software Changes (cont’d.)
General steps (cont’d.)
  Notify appropriate personnel of intent to change
  Back up current system
  Prevent users from accessing system during change
  Keep instructions handy as you install revision
  Implement the change
  Test system fully
  Re-enable access to the system
    Or revert to previous version
  Inform personnel that change is complete
  Record change in the change management system

## Slide 33: Software Changes (cont’d.)
NOS (Network Operating System) upgrades
  Most critical upgrade type
  Involves significant and potentially drastic changes to the way servers and clients operate
  Upgrade requires forethought, product research, and rigorous testing
  Ask and answer significant questions
  Create a project plan
  Complex, far-reaching change
  Ensure appropriate budget, resources, and time

## Slide 34: Software Changes (cont’d.)
Steps in NOS upgrade
  Research
  Project plan
  Proposal
  Evaluation
  Testing
  Training
  Preimplementation
  Implementation
  Postimplementation

## Slide 35: Software Changes (cont’d.)
Reversing a software upgrade
  Software change may create unexpected problems
  Be prepared to reverse an upgrade
Backleveling
  Reverting to previous version of software after attempting upgrade
  No hard-and-fast rules for backleveling
  Always refer to software vendor’s documentation to reverse an upgrade
    For NOS: consult other professionals as well

## Slide 36
Table 15-1 Reversing a software upgrade
Courtesy Course Technology/Cengage Learning

## Slide 37: Hardware and Physical Plant Changes
Required when network component fails or malfunctions
More commonly performed as upgrade
  Increase capacity, improve performance, and add network functionality
Face same issues as software changes
  Proper planning is key
  Follow steps on Pages 712-713 of text

## Slide 38: Hardware and Physical Plant Changes (cont’d.)
Adding or upgrading equipment
  Difficulty determined by past use; experience with hardware or vendor
  Take time to research, evaluate, and test unfamiliar equipment
  Rapid hardware industry changes
    May affect consistency of installed products
  If consistency is a concern
    Purchase as much hardware as possible in single order
    Purchase from same vendor

## Slide 39: Hardware and Physical Plant Changes (cont’d.)
Adding or upgrading equipment (cont’d.)
  Different preparation and implementation requirements for each device type
  Read manufacturer’s instructions
  Gain experience with networking equipment
  Follow general guidelines for each device type
  Devices that are most disruptive and complex to add or upgrade
    Most difficult to remove or backlevel
  Keep safety in mind when upgrading and installing network hardware

## Slide 40: Hardware and Physical Plant Changes (cont’d.)
Cabling upgrades
  Can require significant implementation planning
    Depending on network size
  Troubleshooting cabling problems
    Easier with current and accurate wiring schematics
  Carefully document existing cable before making upgrades
    Ensures future upgrades go smoothly
  Consider upgrading in phases

## Slide 41: Hardware and Physical Plant Changes (cont’d.)
Cabling upgrades (cont’d.)
  Weigh upgrade importance against disruption potential
  Organizations with very small networks
    Upgrade own network cabling
  Larger organizations
    Rely on contractors

## Slide 42: Hardware and Physical Plant Changes (cont’d.)
Backbone upgrades
  Most comprehensive and complex upgrade
  Backbone represents main data conduit
  Requirements
    Extensive planning, personnel efforts, and investment
  Upgrading entire backbone changes the whole network

## Slide 43: Hardware and Physical Plant Changes (cont’d.)
Reversing hardware changes
  Provide way to reverse hardware upgrade
    Reinstall old hardware
  Faulty component: reinstall not possible
  Keep old components safe and nearby
    May need to reinstall
    Refer to it for information

## Slide 44: Summary
Network management
  Assessing, monitoring, and maintaining network devices and connections
Configuration management
  Software and hardware configuration documentation
Network management applications use SNMP to communicate with managed devices
System logs and event logs record conditions
Software and hardware upgrades require planning