## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 9
In-Depth TCP/IP Networking

## Slide 2: Objectives
Describe methods of network design unique to TCP/IP networks, including subnetting, CIDR, and address translation
Explain the differences between public and private TCP/IP networks
Describe protocols used between mail clients and mail servers, including SMTP, POP3, and IMAP4
Employ multiple TCP/IP utilities for network discovery and troubleshooting

## Slide 3: Designing TCP/IP-Based Networks
TCP/IP protocol suite use
  Internet connectivity
  Private connection data transmission
TCP/IP fundamentals
  IP: routable protocol
    Interfaces requires unique IP address
    Node may use multiple IP addresses
  Two IP versions: IPv4 and IPv6
  Networks may assign IP addresses dynamically

## Slide 4: Subnetting
Separates network
  Multiple logically defined segments (subnets)
    Geographic locations, departmental boundaries, technology types
Subnet traffic separated from other subnet traffic
Reasons to separate traffic
  Enhance security
  Improve performance
  Simplify troubleshooting

## Slide 5: Subnetting (cont’d.)
Classful addressing in IPv4
  First, simplest IPv4 addressing type
  Adheres to network class distinctions
  Recognizes Class A, B, C addresses
Drawbacks
  Fixed network ID size limits number of network hosts
  Difficult to separate traffic from various parts of a network

## Slide 6: Subnetting (cont’d.)
Figure 9-1 Network and host information in classful IPv4 addressing
Courtesy Course Technology/Cengage Learning

## Slide 7: Subnetting (cont’d.)
Figure 9-2 Sample IPv4 addresses with classful addressing
Courtesy Course Technology/Cengage Learning

## Slide 8: Subnetting (cont’d.)
IPv4 subnet masks
  Identifies how network subdivided
  Indicates where network information located
  Subnet mask bits
    1: corresponding IPv4 address bits contain network information
    0: corresponding IPv4 address bits contain host information
Network class
  Associated with default subnet mask

## Slide 9: Subnetting (cont’d.)
Table 9-1 Default IPv4 subnet masks
Courtesy Course Technology/Cengage Learning

## Slide 10: Subnetting (cont’d.)
ANDing
  Combining bits
    Bit value of 1 plus another bit value of 1 results in 1
    Bit value of 0 plus any other bit results in 0
  Logic
    1: “true”
    0: “false”

## Slide 11
Table 9-2 ANDing
Courtesy Course Technology/Cengage Learning
Figure 9-3 Example of calculating a host’s network ID
Courtesy Course Technology/Cengage Learning

## Slide 12: Subnetting (cont’d.)
Special addresses
  Cannot be assigned to node network interface
  Used as subnet masks
Examples of special addresses
  Network ID
  Broadcast address

## Slide 13
Table 9-3 IPv4 addresses reserved for special functions
Courtesy Course Technology/Cengage Learning

## Slide 14: Subnetting (cont’d.)
IPv4 subnetting techniques
  Subnetting alters classful IPv4 addressing rules
  IP address bits representing host information change to represent network information
  Reduces usable host addresses per subnet
  Number of hosts, subnets available after subnetting depend on host information bits borrowed

## Slide 15
Table 9-4 Class B subnet masks
Courtesy Course Technology/Cengage Learning

## Slide 16
Table 9-5 IPv4 Class C subnet masks
Courtesy Course Technology/Cengage Learning

## Slide 17: Subnetting (cont’d.)
Calculating IPv4 Subnets
  Formula: 2n −2=Y
    n: number of subnet mask bits needed to switch from 0 to 1
    Y: number of resulting subnets
Example
  Class C network
    Network ID: 199.34.89.0
    Want to divide into six subnets

## Slide 18
Table 9-6 Subnet information for six subnets in a sample IPv4 Class C network
Courtesy Course Technology/Cengage Learning

## Slide 19: Subnetting (cont’d.)
Class A, Class B, and Class C networks
  Can be subnetted
    Each class has different number of host information bits usable for subnet information
    Varies depending on network class and the way subnetting is used
LAN subnetting
  LAN’s devices interpret device subnetting information
  External routers
    Need network portion of device IP address

## Slide 20
Figure 9-4 A router connecting several subnets
Courtesy Course Technology/Cengage Learning

## Slide 21: CIDR (Classless Interdomain Routing)
Also called classless routing or supernetting
Not exclusive of subnetting
  Provides additional ways of arranging network and host information in an IP address
  Conventional network class distinctions do not exist
Example: subdividing Class C network into six subnets of 30 addressable hosts each
Supernet
  Subnet created by moving subnet boundary left

## Slide 22
Figure 9-5 Subnet mask and supernet mask
Courtesy Course Technology/Cengage Learning

## Slide 23: CIDR (cont’d.)
Example: class C range of IPv4 addresses sharing network ID 199.34.89.0
  Need to greatly increase number of default host addresses
Figure 9-6 Calculating a host’s network ID on a supernetted network
Courtesy Course Technology/Cengage Learning

## Slide 24: CIDR (cont’d.)
CIDR notation (or slash notation)
  Shorthand denoting subnet boundary position
  Form
    Network ID followed by forward slash ( / )
    Followed by number of bits used for extended network prefix
  CIDR block
    Forward slash, plus number of bits used for extended network prefix
    Example: /22

## Slide 25: Subnetting in IPv6
Each ISP can offer customers an entire IPv6 subnet
Subnetting in IPv6
  Simpler than IPv4
  Classes not used
  Subnet masks not used
Subnet represented by leftmost 64 bits in an address
Route prefix
  Slash notation is used

## Slide 26
Figure 9-8 Hierarchy of IPv6 routes and subnets
Figure 9-7 Subnet prefix and interface ID in an IPv6 address
Courtesy Course Technology/Cengage Learning
Courtesy Course Technology/Cengage Learning

## Slide 27: Internet Gateways
Combination of software and hardware
Enables different network segments to exchange data
Default gateway
  Interprets outbound requests to other subnets
  Interprets inbound requests from other subnets
Network nodes
  Allowed one default gateway
    Assigned manually or automatically (DHCP)

## Slide 28: Internet Gateways (cont’d.)
Gateway interface on router
  Advantages
    One router can supply multiple gateways
    Gateway assigned own IP address
Default gateway connections
  Multiple internal networks
  Internal network with external networks
    WANs, Internet
  Router used as gateway
    Must maintain routing tables

## Slide 29
Figure 9-9 The use of default gateways
Courtesy Course Technology/Cengage Learning

## Slide 30: Address Translation
Public network
  Any user may access
  Little or no restrictions
Private network
  Access restricted
    Clients, machines with proper credentials
  Hiding IP addresses
    Provides more flexibility in assigning addresses
NAT (Network Address Translation)
  Gateway replaces client’s private IP address with Internet-recognized IP address

## Slide 31: Address Translation (cont’d.)
Reasons for using address translation
  Overcome IPv4 address quantity limitations
  Add marginal security to private network when connected to public network
  Use own network addressing scheme
SNAT (Static Network Address Translation)
  Client associated with one private IP address, one public IP address
  Addresses never change
  Useful when operating mail server

## Slide 32
Figure 9-10 SNAT (Static Network Address Translation)
Courtesy Course Technology/Cengage Learning

## Slide 33: Address Translation (cont’d.)
DNAT (Dynamic Network Address Translation)
  Also called IP masquerading
  Internet-valid IP address might be assigned to any client’s outgoing transmission
PAT (Port Address Translation)
  Each client session with server on Internet assigned separate TCP port number
    Client server request datagram contains port number
  Internet server responds with datagram’s destination address including same port number

## Slide 34
Figure 9-11 PAT (Port Address Translation)
Courtesy Course Technology/Cengage Learning

## Slide 35: Address Translation (cont’d.)
NAT
  Separates private, public transmissions on TCP/IP network
Gateways conduct network translation
  Most networks use router
Gateway might operate on network host
  Windows operating systems
    ICS (Internet Connection Sharing)

## Slide 36: TCP/IP Mail Services
Internet mail services
  Mail delivery, storage, pickup
Mail servers
  Communicate with other mail servers
  Deliver messages, send, receive, store messages
  Popular programs: Sendmail, Microsoft Exchange Server
Mail clients
  Send and retrieve messages to/from mail servers
  Popular programs: Microsoft Outlook, Thunderbird

## Slide 37: SMTP (Simple Mail Transfer Protocol)
Protocol responsible for moving messages
  From one mail server to another
    Over TCP/IP-based networks
Operates at Application layer
  Relies on TCP at Transport layer
Operates from port 25
Provides basis for Internet e-mail service
  Relies on higher-level programs for its instructions
Services provide friendly, sophisticated mail interfaces

## Slide 38: SMTP (cont’d.)
Simple subprotocol
  Transports mail, holds it in a queue
Client e-mail configuration
  Identify user’s SMTP server
    Use DNS: Identify name only
  No port definition
    Client workstation, server assume port 25

## Slide 39: MIME (Multipurpose Internet Mail Extensions)
SMTP drawback: 1000 ASCII character limit
MIME standard
  Encodes, interprets binary files, images, video, non-ASCII character sets within e-mail message
  Identifies each mail message element according to content type
    Text, graphics, audio, video, multipart
Does not replace SMTP
  Works in conjunction with it
Encodes different content types
  Fools SMTP

## Slide 40: POP (Post Office Protocol)
Application layer protocol
  Retrieve messages from mail server
POP3 (Post Office Protocol, version 3)
  Current, popular version
  Relies on TCP; operates over port 110
  Store-and-forward type of service
Advantages
  Minimizes server resources
    Mail deleted from server after retrieval (disadvantage for mobile users)
  Mail server, client applications support POP3

## Slide 41: IMAP (Internet Message Access Protocol)
More sophisticated alternative to POP3
IMAP4: current version
Advantages
  Replace POP3 without having to change e-mail programs
  E-mail stays on server after retrieval
    Good for mobile users

## Slide 42: IMAP (cont’d.)
Features
  Users can retrieve all or portion of mail message
  Users can review messages and delete them
    While messages remain on server
  Users can create sophisticated methods of organizing messages on server
  Users can share mailbox in central location

## Slide 43: IMAP (cont’d.)
Disadvantages
  Requires more storage space, processing resources than POP servers
  Network managers must watch user allocations closely
  IMAP4 server failure
    Users cannot access mail

## Slide 44: Additional TCP/IP Utilities
TCP/IP transmission process
  Many points of failure
    Increase with network size, distance
Utilities
  Help track down most TCP/IP-related problems
  Help discover information about node, network
Nearly all TCP/IP utilities
  Accessible from command prompt
  Syntax differs per operating system

## Slide 45: Ipconfig
Command-line utility providing network adapter information
  IP address, subnet mask, default gateway
Windows operating system tool
  Command prompt window
    Type ipconfig and press Enter
  Switches manage TCP/IP settings
    Forward slash ( / ) precedes command switches
Requires administrator rights
  To change workstation’s IP configuration

## Slide 46
Figure 9-12 Output of an ipconfig command on a Windows workstation
Courtesy Course Technology/Cengage Learning

## Slide 47: Ifconfig
Utility used on UNIX and Linux systems
  Modify TCP/IP network interface settings
  Release, renew DHCP-assigned addresses
  Check TCP/IP setting status
  Runs at UNIX, Linux system starts
    Establishes computer TCP/IP configuration
Used alone or with switches
  Uses hyphen ( - ) before some switches
  No preceding character for other switches

## Slide 48
Figure 9-13 Detailed information available through ifconfig
Courtesy Course Technology/Cengage Learning

## Slide 49: Netstat
Displays TCP/IP statistics, component details, host connections
Used without switches
  Displays active TCP/IP connections on machine
Can be used with switches

## Slide 50
Figure 9-14 Output of a netstat –a command
Courtesy Course Technology/Cengage Learning

## Slide 51: Nbtstat
NetBIOS
  Protocol runs in Session and Transport layers
  Associates NetBIOS names with workstations
  Not routable
    Can be made routable by encapsulation
Nbtstat utility
  Provides information about NetBIOS statistics
  Resolves NetBIOS names to IP addresses
  Useful only on Windows-based operating systems and NetBIOS
    Limited use as TCP/IP diagnostic utility

## Slide 52: Hostname, Host, and Nslookup
Hostname utility
  Provides client’s host name
    Administrator may change
Host utility
  Learn IP address from host name
  No switches: returns host IP address or host name
Nslookup
  Query DNS database from any network computer
    Find the device host name by specifying its IP address
  Verify host configured correctly; troubleshoot DNS resolution problems

## Slide 53
Figure 9-15 Output of a simple nslookup command
Courtesy Course Technology/Cengage Learning

## Slide 54: Dig
Domain information groper
Similar to nslookup
  Query DNS database
  Find specific IP address host name
Useful for diagnosing DNS problems
Dig utility provides more detailed information than nslookup
Flexible: two dozen switches
Included with UNIX, Linux operating systems
Windows system: must obtain third party code

## Slide 55
Figure 9-16 Output of a simple dig command
Courtesy Course Technology/Cengage Learning

## Slide 56: Traceroute (Tracert)
Windows-based systems: tracert
Linux systems: tracepath
ICMP ECHO requests
  Trace path from one networked node to another
  Identifying all intermediate hops between two nodes
Transmits UDP datagrams to specified destination
  Using either IP address or host name
    To identify destination
Several switches available

## Slide 57
Figure 9-17 Output of a traceroute command
Courtesy Course Technology/Cengage Learning

## Slide 58: Mtr (my traceroute)
Comes with UNIX, Linux operating systems
  Route discovery, analysis utility
Combines ping, traceroute functions
  Output: easy-to-read chart
Simplest form
  mtr ip_address or mtr host_name
    Run continuously
    Stop with Ctrl+C or add limiting option to command
Number of switches refine functioning, output
Results misleading
  If devices prevented from responding to ICMP traffic

## Slide 59: Mtr (my traceroute)
Windows operating systems
  Pathping program as command-line utility
  Similar switches to mtr
  Pathping output differs slightly
    Displays path first
    Then issues hundreds of ICMP ECHO requests before revealing reply, packet loss statistics

## Slide 60
Figure 9-18 Output of the mtr command
Courtesy Course Technology/Cengage Learning

## Slide 61: Route
Route utility
  Shows host’s routing table
UNIX or Linux system
  Type route and press Enter
Windows-based system
  Type route print and press Enter
Cisco-brand router
  Type show ip route and press Enter

## Slide 62
Figure 9-19 Sample routing table
Courtesy Course Technology/Cengage Learning

## Slide 63
Table 9-7 Fields in routing table on a UNIX host
Courtesy Course Technology/Cengage Learning

## Slide 64: Route (cont’d.)
Route command
  Add, delete, modify routes
Route command help
  UNIX or Linux system
    Type man route
  Windows system
    Type route ?

## Slide 65: Summary
Subnetting separates network into multiple segments or subnets
Creating subnets involves changing IP address bits to represent network information
CIDR is a newer variation on traditional subnetting
Last four blocks represent interface in IPv6
Gateways facilitate communication between subnets
Different types of address translation protocols exist
Several utilities exist for TCP/IP network discovery, troubleshooting