## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 12
Voice and Video Over IP

## Slide 2: Objectives
Use terminology specific to converged networks
Explain VoIP (Voice over IP) services, PBXs, and their user interfaces
Explain video-over-IP services and their user interfaces
Describe VoIP and video-over-IP signaling and transport protocols, including SIP, H.323, and RTP
Understand QoS (quality of service) assurance methods critical to converged networks, including RSVP and DiffServ

## Slide 3: Terminology
IP telephony (VoIP)
  Any network carrying voice signals using TCP/IP
    Public or private
  Runs over any packet-switched network
Data connection types carrying VoIP signals
  T-carriers, ISDN, DSL, broadband cable, satellite connections, WiFi, WiMAX, HSPA+, LTE, cellular telephone networks

## Slide 4: Terminology (cont’d.)
Internet telephony
  VoIP calls carried over Internet
  Advantages: breadth, low cost
Private lines
  Carry VoIP calls
  Effective and economical
  Network congestion control capabilities
  Better sound quality

## Slide 5: Terminology (cont’d.)
Nondata applications on converged networks
  IPTV (IP television)
  Videoconferencing
    Multiple participants communicate and collaborate via audiovisual means
  Streaming video
    Compressed video delivered in continuous stream
  Webcasts
    Streaming videos supplied via the Web

## Slide 6: Terminology (cont’d.)
Multicasting
  One node transmits same content to every client in group
Video over IP
  IPTV, videoconferencing, streaming video, IP multicasting
Unified communications (unified messaging) service
  Several communication forms available from single user interface

## Slide 7: VoIP Applications and Interfaces
Reasons for implementing VoIP
  Lower voice call cost
  New, enhanced features and applications
  Centralize voice and data network management
Voice and data configurations
  Traditional telephone (sends, receives analog signals)
  Telephone specially designed for TCP/IP transmission
  Computer with microphone, speaker, VoIP client software
  Mixture of these types

## Slide 8: Analog Telephones
Traditional telephone used for VoIP
  Signals converted to digital form
Codec
  Method of compressing, encoding, analog signals
ATA (analog telephone adapter)
  Card within computer workstation
  Externally attached device
  Telephone line connects to RJ-11 adapter port
  Converts analog voice signals to IP packets

## Slide 9
Figure 12-1 ATA (analog telephone adapter)
Courtesy of Grandstream Networks, Inc.

## Slide 10: Analog Telephones (cont’d.)
Alternate analog-to-digital conversion method
  Connect analog telephone line to switch, router, or gateway
  Convert analog voice signals into packet
  Issue packet to data network
  Vice versa

## Slide 11
Figure 12-2 VoIP router
Photo of SmartNode™4520 Analog VoIP router from Patton Electronics , Co.

## Slide 12: Analog Telephones (cont’d.)
Digital PBX (private branch exchange)
  More commonly called IP-PBX
  Telephone switch connecting and managing calls within private organization
  Accepts, interprets analog and digital voice signals
  Connects with traditional PSTN lines, data networks
  Transmits, receives IP-based voice signals to and from other network connectivity devices
  Packaged with sophisticated software

## Slide 13
Figure 12-3 IP-PBX
Courtesy of Epygi Technologies, Ltd.

## Slide 14: Analog Telephones (cont’d.)
Hosted PBX
  Exists on the Internet
  Separate provider for call management services
  May also be called virtual PBXs
    Trademark of VirtualPBX company
Advantage of Hosted PBXs
  No installation or maintenance of hardware and software for call completion and management

## Slide 15: Analog Telephones (cont’d.)
Traditional telephone connects to analog PBX
  Then connects to voice-data gateway
Gateway connects traditional telephone circuits with TCP/IP network
  Internet or private WAN
Gateway actions
  Digitizes incoming analog voice signal
  Compresses data
  Assembles data into packets
  Issues packets to packet-switched network

## Slide 16
Figure 12-4 Integrating VoIP networks and analog telephones
Courtesy of Course Technology/Cengage Learning

## Slide 17: IP Telephones
IP telephones (IP phones)
  Transmit, receive only digital signals
  Voice immediately digitized, issued to network in packet form
  Requires unique IP address
  Looks like traditional touch-tone phone
  Connects to RJ-45 wall jack
  Connection may pass through connectivity device before reaching IP-PBX

## Slide 18
Figure 12-5 Accessing a VoIP network from IP phones
Courtesy of Course Technology/Cengage Learning

## Slide 19: IP Telephones (cont’d.)
IP telephone features
  Speed-dialing
  Call hold
  Transfer, forward
  Conference calling
  Voice-mail access
  Speakers, microphones, LCD screen
  Mobile and wired styles
  Some can act as Web browsers
  Easily moved from office to office

## Slide 20: IP Telephones (cont’d.)
Conventional analog telephone
  Obtains current from local loop
  Current used for signaling (ring, dial tone)
IP telephones
  Need electric current
  Not directly connected to local loop
  Most use separate power supply
    Susceptible to power outages
    Requires assured backup power sources
  Some use PoE (power over Ethernet)

## Slide 21
Figure 12-6 An IP phone
Courtesy of Grandstream Networks, Inc.

## Slide 22: Softphones
Computer programmed to act like IP telephone
  Provide same calling functions
  Connect to network; deliver services differently
Prerequisites
  Computer minimum hardware requirements
  IP telephony client installed
  Digital telephone switch communication
  Full-duplex sound card
  Microphone, speakers
Softphone example: Skype

## Slide 23: Softphones (cont’d.)
Graphical interface
  Presented after user starts softphone client software
  Customizable
Versatile connectivity
  VoIP solution for traveling employees and telecommuters
Convenient, localized call management
  Call tracking
    Date, time, duration, originating number, caller names
  Simplifies recordkeeping and billing

## Slide 24
Figure 12-7 Softphone interface
Courtesy of CounterPath Corporation

## Slide 25
Figure 12-8 Connecting softphones to a converged network
Courtesy of Course Technology/Cengage Learning

## Slide 26: Video-over-IP Applications and Interfaces
Cisco Systems estimate
  By 2015, over two-thirds of Internet traffic will be video traffic
Factors fueling growth
  Large quantity of video content available
  Increasing number of devices accessing Internet
  Decreasing cost of bandwidth, equipment
Video-over-IP services categories
  Streaming video, IPTV, videoconferencing

## Slide 27: Streaming Video
Simplest among video-over-IP applications
  Basic computer hardware, software requirements
Video-on-demand
  Files stored on video streaming server
  Popular
  Viewer chooses video when convenient
    Views using Web browser
Streaming video can be issued live
  From source directly to user

## Slide 28: Streaming Video (cont’d.)
Drawbacks of live stream
  Content may not be edited before distribution
  Viewers must connect with stream when issued
Video-on-demand benefits
  Content viewed at user’s convenience
  Viewers control viewing experience
    Pause, rewind, fast-forward capabilities

## Slide 29
Figure 12-9 Video-on-demand and live streaming video
Courtesy of Course Technology/Cengage Learning

## Slide 30: Streaming Video (cont’d.)
Consider number of clients receiving each service
  Point-to-point video over IP
  Point-to-multipoint video over IP
    Not the same as multicast transmission
Unicast transmissions
  Single node issues data stream to one other node
  Example: CSPAN source issues signals to each viewer
Network classification: public or private
  Most streaming video occurs over public networks

## Slide 31: IPTV (IP Television)
Telecommunications carrier, cable company networks
  High-bandwidth Internet connections
  IPTV digital television signals
  Digital video valued as an added service
  Investing money into hardware, software
Elements of delivering digital video to consumers
  Telco accepts video content at a head end
  Telco’s CO (central office) servers provide management services
  Video channel assigned to multicast group

## Slide 32
Figure 12-10 A telecommunications carrier’s IPTV network
Courtesy of Course Technology/Cengage Learning

## Slide 33: IPTV (cont’d.)
IPTV multicasting advantages
  Simple content delivery management
    Issue one multicast transmission to entire group
  Local loop capacity issues
    Most rely on copper to home (limits throughput)
    Overwhelming local loop
    Solution: Telco transmits only content ordered
IGMP (Internet Group Management Protocol)
  Manages multicasting
  Routers communicate using multicast routing protocol

## Slide 34: IPTV (cont’d.)
Compressed, digital video signal travels like data signal
  DSL, WIMAX
Advantage of delivering video over telcom or cable network
  Company controls connection end to end
    Can monitor and adjust QoS (quality of service)

## Slide 35: Videoconferencing
Unidirectional video-over-IP services
  Video delivered to user who only watches content
Videoconferencing
  Full-duplex connections
    Participants send, receive audiovisual signals
  Real time
  Benefits
    Cost savings, convenience
    Replace face-to-face business meetings
    Allow collaboration

## Slide 36: Videoconferencing (cont’d.)
Videoconferencing uses
  Telemedicine
  Tele-education
  Judicial proceedings
  Surveillance
Hardware, software requirements
  Means to generate, send, receive audiovisual signals
    Computer workstation with cameras, microphones, software
    Video terminal or video phone

## Slide 37
Figure 12-12 Videophone
Courtesy of Grandstream Networks

## Slide 38: Videoconferencing (cont’d.)
Video bridge
  Manages multiple audiovisual sessions
    Participants can see, hear each other
  Conference server
    Hardware or software
Leased Internet-accessible video bridging services
  Occasional videoconference use
Video bridge depends on signaling protocols

## Slide 39: Signaling Protocols
Signaling
  Information exchange between network components, system
  Establishing, monitoring, releasing connections
  Controlling system operations
Signaling protocols
  Set up, manage client sessions
  Perform several functions
Early VoIP: proprietary signaling protocols
Today: standardized signaling protocols

## Slide 40: H.323
ITU standard describing architecture, protocols
  Establishing, managing packet-switched network multimedia sessions
Supports voice, video-over-IP services
Terms
  H.323 terminal
  H.323 gateway
  H.323 gatekeeper
  MCU (multipoint control unit)
  H.323 zone

## Slide 41
Figure 12-13 An H.323 zone
Courtesy of Course Technology/Cengage Learning

## Slide 42: H.323 (cont’d.)
H.225 and H.245 signaling protocols
  Specified in H.323 standard
  Operate at Session layer
H.225 handles call or videoconference signaling
H.245 ensures correct information type formatting
  Uses logical channels
H.323 standard
  Specifies protocol interoperability
    Presentation layer: coding, decoding signals
    Transport layer

## Slide 43: H.323 (cont’d.)
Codified in 1996
Early version suffered slow call setup
Revised several times
Remains popular signaling protocol
  Large voice and video networks

## Slide 44: SIP (Session Initiation Protocol)
Application layer signaling, multiservice control protocol, packet-based networks
  Performs similar functions as H.323
Modeled on HTTP
Reuse existing TCP/IP protocols
  Session management, enhanced services
Modular and specific
Limited capabilities compared to H.323
  Example: no caller ID

## Slide 45: SIP (cont’d.)
SIP network components
  User agent
  User agent client
  User agent server
  Registrar server
  Proxy server
  Redirect server

## Slide 46
Figure 12-14 An H.323 zone
Courtesy of Course Technology/Cengage Learning

## Slide 47: SIP (cont’d.)
Advantages of SIP over H.323
  Simplicity
  Fewer instructions to control call
  Consumes fewer processing resources
  More flexible
SIP and H.323
  Regulate call signaling, control for VoIP or video-over-IP clients and servers
  Do not account for communication between media gateways

## Slide 48: MGCP (Media Gateway Control Protocol) and MEGACO (H.248)
Media gateway
  Accepts PSTN lines
  Converts analog signals into VoIP format
  Translates between different signaling protocols
Information uses different channels than control signals
  Also different logical and physical paths
  Expedites information handling
Gateways still need to exchange and translate signaling and control information

## Slide 49: MGCP and MEGACO (cont’d.)
MGC (media gateway controller)
  Computer managing multiple media gateways
  Facilitates exchange of call signaling information
  Also called a softswitch
  Advantageous on large VoIP networks
MGCP (Media Gateway Control Protocol)
  Used on multiservice networks supporting many media gateways
  Operate with H.323 or SIP
  Older protocol

## Slide 50
Figure 12-15 Use of an MGC (media gateway controller)
Courtesy of Course Technology/Cengage Learning

## Slide 51: MGCP and MEGACO (cont’d.)
MEGACO
  Newer protocol
  Performs same functions as MGC
  Different commands and processes
  Operates with H.323 or SIP
  Superior to MGCP
  Supports ATM
  Developed by ITU and IETF

## Slide 52: Transport Protocols
MEGACO, MGC
  Communicate information about voice, video session
Different protocol set delivers voice or video payload
  Transport layer
Transport layer protocols
  TCP: connection oriented protocol
    Delivery guarantees
  UDP: connectionless protocol
    No accountability; preferred for real-time applications
    Packet loss tolerable if additional protocols overcome UDP shortcomings

## Slide 53: RTP (Real-time Transport Protocol)
Operates at Application layer
Relies on UDP at the Transport layer
Applies sequence numbers to indicate:
  Destination packet assembly order
  Packet loss during transmission
Assigns packet timestamp
  Receiving node
  Compensates for network delay
  Synchronizes signals
No mechanism to detect success

## Slide 54: RTCP (Real-time Transport Control Protocol)
Provides quality feedback to participants
  Packets transmitted periodically
  RTCP allows for several message types
RTCP value
  Depends on clients’, applications’ information use
Not mandatory on RTP networks
RTP and RTCP
  Provide information about packet order, loss, delay
  Cannot correct transmission flaws

## Slide 55: QoS (Quality of Service) Assurance
VoIP, video over IP transmission difficulty
  Caused by connection’s inconsistent QoS
Preventing delays, disorder, distortion
  Requires more dedicated bandwidth
  Requires techniques ensuring high QoS
QoS measures network service performance
  High QoS: uninterrupted, accurate, faithful reproduction
Improvements to QoS made in recent years
  Service quality now comparable to PSTN, cable TV

## Slide 56: RSVP (Resource Reservation Protocol)
Transport layer protocol
  Reserves network resources prior to transmission
Creates path between sender, receiver
  Provides sufficient bandwidth
  Signal arrives without delay
Issues PATH statement via RSVP to receiving node
  Indicates required bandwidth, expected service level
Two service types
  Guaranteed service
  Controlled-load service

## Slide 57: RSVP (cont’d.)
Router marks transmission’s path
  Routers issue PATH message
  Destination router issues Reservation Request (RESV) message
    Follows same path in reverse
    Reiterates information
    Routers allocate requested bandwidth
    Sending node transmits data

## Slide 58: RSVP (cont’d.)
RSVP messaging separate from data transmission
  Does not modify packets
  Specifies and manages unidirectional transmission
    Resource reservation process takes place in both directions
RSVP emulates circuit-switched path
  Provides excellent QoS
Drawback: high overhead
  Acceptable on small networks
  Larger networks use streamlined techniques: DiffServ

## Slide 59: DiffServ (Differentiated Service)
Addresses QoS issues through traffic prioritization
Differs from RSVP
  Modifies actual IP datagram
  Accounts for all network traffic
Can assign different streams different priorities
To prioritize traffic
  IPv4 datagram: DiffServ field
  IPv6 datagram: Traffic Class field

## Slide 60: DiffServ (cont’d.)
Two forwarding types
  EF (Expedited Forwarding)
    Data stream assigned minimum departure rate
    Circumvents delays
  AF (Assured Forwarding)
    Data streams assigned different router resource levels
    Prioritizes data handling
    No guarantee of on time, in sequence packet arrival

## Slide 61: MPLS (Multiprotocol Label Switching)
Modifies data streams at Network layer
Replaces IP datagram header with label:
  At first router data stream encounters
  Next router revises label
  Label contains packet forwarding information
Considers network congestion
Very fast forwarding
Destination IP address compared to routing tables
  Forward data to closest matching node

## Slide 62: Summary
VoIP services carry voice signals over TCP/IP protocol
Four ways to connect VoIP clients to IP networks
Streaming video can be delivered live or on-demand
IPTV television signals travel over packet-switched connections
Video bridges manage communication for videoconferences
H.323 standard
  Describes architecture and protocols for managing multimedia sessions on a packet-switched network